## Slide 1: UNIT - II
Wireless WANS AND MANS

## Slide 2: Syllabus
The Cellular Concept
Cellular Architecture
The First-Generation Cellular Systems
The Second-Generation Cellular Systems
The Third-Generation Cellular Systems
Wireless in Local Loop
IEEE 802.16 Standard
HIPERACCESS

## Slide 3: Syllabus
The Cellular Concept
Cellular Architecture
The First-Generation Cellular Systems
The Second-Generation Cellular Systems
The Third-Generation Cellular Systems
Wireless in Local Loop
IEEE 802.16 Standard
HIPERACCESS

## Slide 4: The Cellular Concept
  Capacity Enhancement
  Channel Allocation Algorithms
  Handoffs

## Slide 5: The Cellular Concept
The cellular concept is a novel way to ensure efficient utilization of the available radio spectrum.
The area to be covered by a cellular network is divided into cells, which are usually considered to be hexagonal.
This is because, of the shapes which can completely cover a two-dimensional region without overlaps, such as the triangle, square, and hexagon, the hexagon most closely resembles the nearly circular coverage area of a transmitter.
An idealized model of the cellular radio system consists of an array of hexagonal cells with a base station (BS) located at the center of each cell.
The available spectrum in a cell is used for uplink channels for mobile terminals (MTs) to communicate with the BS, and for downlink channels, for the BS to communicate with MTs.

## Slide 6: The Cellular Concept
The fundamental and elegant concept of cells relies on frequency reuse, i.e, the usage of the same frequency by different users separated by a distance, without interfering with each other.
A cluster is a group of cells which uses the entire radio spectrum.
The cluster size N is the number of cells in each cluster.
No two cells within a cluster use channels of the same frequency.
Clustering ensures that cells which use the same frequency are separated by a minimum distance, called the reuse distance D.
Cells that use different sets of frequencies are labeled differently, and the outlined set of seven cells forms a cluster.

## Slide 7: The cellular concept

## Slide 8: The Cellular Concept
Two types of interference come into play when the cellular concept is used in the design of a network.
The first one is the co-channel interference which results from the use of same frequencies in cells of different clusters.
The reuse distance should be such that co-channel interference does not adversely affect the signal strength.
The second one is the adjacent channel interference which results due to usage of adjacent frequencies within a cluster.
The channel assignment to different cells within the cluster must minimize adjacent channel interference by not assigning neighboring frequencies to the same cell.
The advantage of the cellular concept is that it can increase the number of users who can be supported in a given area.

## Slide 9: Capacity Enhancement
Each cellular service provider is allotted a certain band of frequencies.
Considering the interference constraints, this restricts the number of channels that can be allotted to each cell.
So, methods have been devised to enhance the capacity of cellular networks.
The main reasons for reduction of cellular network capacity are off-
  center placement of antennas in the cell
  limited frequency reuse imposed by a strict clustering scheme
  inhomogeneous propagation conditions

## Slide 10: Capacity Enhancement
The nearest BS is not always the best for a mobile station, due to shadowing, reflections, and other propagation-based features.
The simplistic model of cellular networks has to be modified to account for these variations.
Few methods used to improve the capacity of cellular networks are-
  Cell-Splitting
  Sectorization
  Power Control

## Slide 11: Cell-Splitting
Non-uniform traffic demand patterns create hotspot regions in cellular networks, which are small pockets with very high demand for channel access.
In order to satisfy QoS constraints, the blocking probability in a hotspot region must not be allowed to shoot up.
This gave rise to the concept of cell-splitting.
A different layer of cells which are smaller in size, and support users with lower mobility rates, is overlaid on the existing (macro-cells) cellular network. These are called micro-cells.
While macro-cells typically span across tens of kilometers, micro-cells are usually less than 1 Km in radius.
Very small cells called pico-cells, of a few meters’ radius, are also in use to cover indoor areas.

## Slide 12: Cell-Splitting

## Slide 13: Cell-Splitting
Depending on the demands in traffic at a given point of time, channels can be allocated explicitly for the micro-cellular layer, or a sharing algorithm can be envisaged with the macro-cellular layer, by which channels can be allotted to the micro-cells as the demand arises.
Users with lower rates of mobility are handled by the layer of smaller cell size.
If a highly mobile user is handled by the micro-cellular layer, there is an overhead of too many handoffs.
The handoffs may not be fast enough to let the call continue uninterrupted.

## Slide 14: Sectorization
This concept uses space division multiple access (SDMA) for more channels be reused within a shorter distance.
Antennas are modified from omnidirectional to sectorized, so that their signals are beamed only in a particular sector, instead of being transmitted symmetrically all around.
This greatly reduces the downlink interference.
A cell is normally partitioned into three 120-degree sectors or six 60-degree sectors.
Further, the antennas can be down-tilted to reduce co-channel interference even more.
Below figure shows the difference between omnidirectional and 60-degree sectored antennas.
Reduction in interference allows shorter reuse distance, and hence increases capacity.

## Slide 15: Sectorization

## Slide 16: Power Control
Cellular networks face the “near-far” problem.
An MT which is very close to the BS receives very strong signals from the BS, and its signals are also extremely strong at the BS.
This can possibly drown out a weak signal of some far-away MT which is on an adjacent frequency.
To avoid this problem, the BS must issue power control orders to the MTs to receive a fairly constant, equal power from all MTs, irrespective of their distance from the BS.
MTs which are farther away from the BS transmit at higher power than nearby MTs, so that the received power at the BS is equal.
This saves power for the MTs near the BS, and avoids excessive interference.
Reduction in interference increases the capacity of the cellular network.

## Slide 17: Channel Allocation Algorithms
Efficient allocation of channels to the different cells can greatly improve overall throughput of the network, in terms of the number of calls supported successfully.
The channel allocation algorithms that can be used vary greatly in complexity and effectiveness.
There are three types of Channel allocation algorithms are there-
  Fixed channel allocation algorithms
  Dynamic channel allocation algorithms
  Hybrid channel allocation algorithms

## Slide 18: Fixed channel allocation algorithms
Fixed channel allocation algorithms allot a set of channels to each cell, and the number of channels per cell is determined a priori.
Cells may be allowed to borrow some channels from their neighboring cells to tide over temporary increase in demand for channels.
This should not violate the minimum reuse distance constraints.
So, one borrowing may prevent some other cells from borrowing certain channels, which bring identical frequencies into use too close to each other.
This is termed “channel locking.”
The main drawback of fixed channel allocation algorithms is that they assume a constant, or at least a predictable, distribution of load over the different cells.
But, in reality, demands are very unpredictable, which may lead to a scarcity of channels in some cells and an excess in others.

## Slide 19: Dynamic channel allocation algorithms
Dynamic channel allocation algorithms do not have any local channels allotted to cells.
The decision of which channel to lend is made dynamically.
This makes dynamic algorithms extremely flexible and capable of dealing with large variations in demand, but they involve a lot of computation.
Dynamic algorithms require a centralized arbitrator to allocate channels, which is a bottleneck.
Hence, distributed channel allocation algorithms are preferred, especially for micro-cells.
All BSs look at the local information about their possible interferers, and decide on a suitable allocation of channels to maximize bandwidth utilization.

## Slide 20: Hybrid channel allocation algorithms
The hybrid channel allocation schemes give two sets of channels to each cell; A is the set of local channels and B is the set of borrowable channels.
Cells allow borrowing only from set B, and reallocate calls to their local channel set as soon as possible.
The hybrid allocation algorithms introduce some flexibility into the channel allocation scheme.
A subset of the channels can be borrowed to account for temporary variations in demand, while there is a minimum guarantee of channels for all cells at all times.
These algorithms are intermediate in terms of complexity and efficiency of bandwidth utilization.

## Slide 21: Handoffs
An important concept that is essential for the functioning of cellular networks is handoffs, also called handovers.
When a user moves from the coverage area of one BS to the adjacent one, a handoff has to be executed to continue the call.
There are two main parts to the handoff procedure:
  The first is to find an uplink-downlink channel pair from the new cell to carry on the call
  The second is to drop the link from the first BS

## Slide 22: Issues Involved in Handoffs
Optimal BS selection
Ping-pong effect
Data loss
Detection of handoff requirement

## Slide 23: Handoff Quality
Handoff quality is measured by a number of parameters, and the performance of a handoff algorithm is judged in terms of how it improves these parameters.
Some of the measures of handoff quality are as follows:
  Handoff delay
  Duration of interruption
  Handoff success
  Probability of unnecessary handoff

## Slide 24: Improved Handoff Strategies
Several improvements have been explored over the conventional hard handoff method, in order to tackle the issues related to handoffs.
  Prioritization
  Relative signal strength
  Soft handoffs
  Predictive handoffs
  Adaptive handoffs