## Slide 1: Cellular Architecture

## Slide 2: Cellular Architecture
Every cell has a BS to which all the MTs in the cell transmit.
The BS acts as an interface between the mobile subscriber and the cellular radio system.
The BSs are themselves connected to a mobile switching center (MSC), as shown in below figure.
The MSC acts as an interface between the cellular radio system and the public switched telephone network (PSTN).
It performs overall supervision and control of the mobile communications, which include location update, call delivery, and user identification.

## Slide 4: Cellular Architecture
The authentication center (AuC) validates the MTs by verifying their identity with the equipment identity register (EIR).
The MSCs are linked through a signaling system 7 (SS7) network, which controls the setting up, managing, and releasing of telephone calls.
The SS7 protocol introduces certain nodes called signaling transfer points (STPs) which help in call routing.

## Slide 5: Cellular Architecture
A subscriber in a mobile network should be efficiently traced to deliver calls to him/her, and he/she should be able to access the network through the mobile end-system, irrespective of his/her location.
This involves management of different databases in the cellular network architecture, and is called location management.
The method used currently for location management requires the MT, also called the mobile station (MS), to report its position to the network periodically.
The network stores the location information of each MT in location databases and this information is retrieved during call delivery.

## Slide 6: Cellular Architecture
In the current location management scheme, each user is permanently associated with the home location register (HLR) in his/her subscribed cellular network.
This HLR contains the user profile consisting of the services subscribed by the user (such as SMS and paging), billing information, and location information.
The visitor location register (VLR) maintains the information regarding roaming users in the cell.
VLRs download the information from the users’ respective HLRs.

## Slide 7: Cellular Architecture
The number and placement of the VLRs vary among networks.
Registration of an MT in a new cell entails updates of its HLR, and the VLRs of its old and new cells.
For ease of management, many cells may be grouped into one registration area (RA) and updates performed only on movement out of the RA.
Delivery of a call requires tracing the current location of the handset by requesting the information from the HLR.

## Slide 8: Cellular Architecture
Recent improvements in location management include the use of distributed databases and replication of user profiles to enable faster access to user information.
Partition-based architectures have been used to group MSCs into partitions, and update databases only if the MT moves out of the partition.
This greatly reduces the number of updates, but the size of the database to be maintained at each partition increases.