## Slide 1: THE FIRST-GENERATION CELLULAR SYSTEMS

## Slide 2: THE FIRST-GENERATION CELLULAR SYSTEMS
The first implementations of the cellular concept constitute the first-generation (1G) systems.
These systems, such as the advanced mobile phone system (AMPS) in the United States and Nordic mobile telephony (NMT) deployed in several European countries, are analog-based (i.e., they employ analog modulation and send information as a continuously varying waveform).

## Slide 3: Advanced Mobile Phone System
AMPS divides the 800 MHz part of the frequency spectrum into several channels, each 30 KHz wide.
The cellular structure uses a cluster size of seven, and each cell is roughly 10-20 Km across.
The AMPS system uses 832 full-duplex channels, with FDM to separate the uplink and downlink channels.
The channels are classified into four main categories:
  downlink control channels for system management
  downlink paging channels for paging an MT (locating an MT in the network and alerting it when it receives a call)
  bidirectional access channels for call setup and channel assignment
  bidirectional data channels to carry user voice/data
AMPS provides a maximum data transmission rate of 10 Kbps.

## Slide 4: Advanced Mobile Phone System
When the MT is powered on, it scans for the most powerful control channel and broadcasts its 32-bit serial number and 10-digit telephone number on it.
The BS which hears this broadcast registers the MT with the mobile switching office (MSO), and informs the HLR of the MT of its present location.
The MT updates its position once every 15 minutes.

## Slide 5: Advanced Mobile Phone System
To make a call, the MT sends the number to be called through an access channel.
The BS sends this request to the MSO, which assigns a duplex channel for the call.
MTs are alerted to incoming calls through the paging channel.
The call is routed through the home to its current location.
Once the MT is located, it takes up the call on the allotted voice channel.

## Slide 6: Advanced Mobile Phone System
In order to conserve the battery power of the handset, the MT goes into a “sleep state” when it is idle.
The designed sleep time is 46.3 ms in the AMPS system.
The MT periodically wakes up to scan the paging channel and check if there is any call addressed to it.

## Slide 7: Advanced Mobile Phone System
The service of a mobile network has similar measures of performance like that of a wired network.
The concept of trunking, used in all communication networks, exploits the statistical behavior of users to enable a fixed number of channels to be shared by a much larger number of users.
The grade of service (GoS) of a trunked network is a measure of accessibility of the network during its peak traffic time.
GoS is specified as the probability of a call being blocked, or experiencing a queuing delay greater than a threshold value.
The AMPS system was designed for GoS of 2% blocking.