## Slide 1: THE SECOND-GENERATION CELLULAR SYSTEMS

## Slide 2: THE SECOND-GENERATION CELLULAR SYSTEMS
  Global System for Mobile Communications
  Data Over Voice Channel
  GSM Evolution of Data Services

## Slide 3: THE SECOND-GENERATION CELLULAR SYSTEMS
As mentioned earlier, 1G systems are analog which leads to the following problems:
  (i) No use of encryption (1G systems do not encrypt traffic to provide privacy).
  (ii) Inferior call quality (This is due to analog traffic which is degraded by interference).
  (iii) Spectrum inefficiency (This is because at any given time a channel is allocated to only one user, regardless of whether the user is active (speaking) or not).

## Slide 4: THE SECOND-GENERATION CELLULAR SYSTEMS
The second-generation (2G) systems, the successors of 1G systems, are digital (clear signal) and thus they overcome the deficiencies of 1G systems.
In 2G the user traffic (digital or digitized voice) must be converted into radio waves (analog signals) before it can be sent (between MT and BS).
A 2G system is called personal communications services (PCS) in the marketing literature.
There are several 2G standards followed in various parts of the world. Some of them are-
  Global System for Mobile communications (GSM) in Europe
  Digital-AMPS (DAMPS) in United States
  Personal Digital Cellular (PDC) in Japan

## Slide 5: Global System for Mobile Communications
GSM is an extremely popular 2G system, which is fully digital, used across over 100 countries.
There are four variants of GSM:
  Operating around 900 MHz [This first variant reuses the spectrum intended for Europe’s analog total access communication system (TACS)]
  Operating around 1,800 MHz [licensed in Europe specifically for GSM. This variant is sometimes called digital communications network (DCN)]
  Operating around 1,900 MHz (used in United States for several different digital networks)
  Operating around 450MHz (latest variant for replacing aging analog networks based on NMT system)
Apart from voice service, GSM also offers a variety of data services.

## Slide 6: Global System for Mobile Communications
The modulation scheme used in GSM is Gaussian minimum shift keying (GMSK).
GSM uses frequency duplex communication, and each call is allotted a duplex channel.
The duplex channels are separated by 45 MHz.
Every channel is of 200 KHz bandwidth.
GSM uses FDM to separate the channels.
The downlink (BSMT) channels are allotted 935-960 MHz, and the uplink (MT-BS) channels are on 890-915 MHz as shown in below Figure.

## Slide 8: Global System for Mobile Communications
The uplink “frame” of eight slots is shifted by a delay of three slots from the downlink frame, so that the MT does not have to send and receive at the same time.
A procedure called adaptive frame alignment is used to account for propagation delay.
An MT which is far away from the BS starts its frame transmission slightly ahead of the actual slot commencement time, so that the reception at the BS is synchronized to the frame structure.
Each physical channel is divided into eight periodic time slots (each of which is 0.577 ms duration), which are time-shared between as many as eight users (logical channels) using TDMA.
A complete cycle of eight time slots is called a (TDMA) frame.

## Slide 9: Data Over Voice Channel
Cellular systems were primarily designed to support voice calls only.
But the demand for supporting other data services, ranging from short messages to Web browsing, slowly emerged.
It was realized that cellular networks have to be modified to support data services.
The main problems in using a voice network for data transmission are-
  Signal distortion
  Handoff error
  Interfacing with fixed network

## Slide 10: Data Over Voice Channel
The main problem is in making the network recognize a data call, and handle it differently from a voice call, by probably disabling some optimizations made on voice calls.
Some possible solutions that have been suggested are
  A control message could be transmitted all along the path of the call, to indicate a data call so that voice coding can be disabled.
  A two-stage dial-up operation can be used, first to the cellular carrier and then to the subscriber. The carrier has different numbers for each service it offers. For example, to set up a data call with an MT, the cellular carrier is first dialed, and it then informs the MT of a data call.
  A subscriber could be assigned separate subscriber numbers for each service he/she opts for.

## Slide 11: GSM Evolution of Data Services
GSM and other 2G standards started providing data services overlaid on the cellular network.
This was meant to be a stop-gap arrangement before the third-generation (3G) networks could be formally deployed, and these data services constituted the 2.5G of cellular networks.
It started out with small messages through SMS, and today, Web-browsing is possible over the mobile network.
Some of the popular data services provided over GSM are-
  Short Messaging Service (SMS)
  High-Speed Circuit-Switched Data (HSCSD)
  General Packet Radio Service (GPRS)
  Enhanced Data Rates for GSM Evolution (EDGE)
  Cellular Digital Packet Data (CDPD)

## Slide 12: Short Messaging Service (SMS)
SMS is a connectionless transfer of messages, each up to 160 alphanumeric characters in length.
To send longer messages, small packets are either concatenated at the receiver, or the sender sends compressed messages.
SMS can perform point-to-point data service as well as broadcast throughout the cell.
The message transfer takes place over the control channel.

## Slide 13: High-Speed Circuit-Switched Data (HSCSD)
HSCSD is a simple upgrade to GSM.
It is a circuit-switched protocol for large file transfers and multimedia data transmissions.
Contrary to GSM (one TDMA slot/user), it allots up to eight TDMA slots per user and hence the increased data rates.
By using up to four consecutive time slots, HSCSD can provide a data rate of 57.6 Kbps to a user.
Its disadvantage is that it increases blocking probability by letting the same user occupy more time slots that could have otherwise been used for many voice calls.

## Slide 14: General Packet Radio Service (GPRS)
GPRS, which promises to give every user a high-capacity connection to the Internet, uses TCP/IP and X.25 and offers data rates up to 171.2 Kbps, when all eight time slots of a GSM radio channel are dedicated to GPRS.
Being a packetized service, GPRS does not need an end-to-end connection.
It uses radio resources only during actual data transmission.
So, GPRS is extremely well-suited for short bursts of data such as e-mail and faxes, and non-real-time Internet usage.
Implementation of GPRS on the existing GSM network requires only the addition of packet data switching and gateway nodes, and has minimal impact on the already established network.

## Slide 15: Enhanced Data Rates for GSM Evolution (EDGE)
EDGE, also referred to as enhanced GPRS or EGPRS, inherits all the features from GSM and GPRS, including the eight-user TDMA slot structure and even the slot length of 0.577 ms.
It uses 8-PSK (octal PSK) modulation which triples the capacity compared to GSM.
It provides cellular operators with a commercially viable and attractive method to support multimedia services.
As 8-PSK is more susceptible to errors than GMSK, EDGE has nine different modulation and coding schemes (air interfaces), each designed for a different quality connection.

## Slide 16: Cellular Digital Packet Data (CDPD)
CDPD is a packet-based data service that can be overlaid on AMPS and IS-136 systems.
It supports a connectionless network service, where every packet is routed independently to the destination.
The advantage of CDPD lies in being able to detect idle voice channels of the existing cellular network, and use them to transmit short data messages without affecting the voice network.
The available channels are periodically scanned and a list of probable candidates for data transmission is prepared.
The system uses channel sniffing to detect channels which have been idle and can carry data.

## Slide 17: Cellular Digital Packet Data (CDPD)
The system must continuously hop channels so that it does not block a voice call on a channel it is currently using.
To avoid this channel stealing from the voice network, channel hopping is performed very rapidly, at the rate of once every ten seconds.
Usually, a timed hop is performed by using a dwell timer, which determines how long the CDPD can use a channel.
If the channel has to be allocated in the meantime to a voice call, CDPD performs an emergency hop.
So, it is essential to find alternate idle channels in real time to ensure that data is not lost.