## Slide 1: The Third-Generation Cellular Systems

## Slide 2: The Third-Generation Cellular Systems
  3G Standards
  The Problems with 3G Systems

## Slide 3: The Third-Generation Cellular Systems
The aim of the third-generation (3G) cellular system is to provide a virtual home environment, defined as a uniform and continuous presentation of services, independent of location and access.
This requires very stringent QoS adherence, and highly effective and optimized architectures, algorithms, and operations of the network elements.
The networks should contain advanced algorithms to handle location information retrieval and update, handoffs, authentication, call routing, and pricing.

## Slide 4: The Third-Generation Cellular Systems
From the user point of view, the 3G systems with very high-speed wireless communications (up to 2 Mbps) plan to offer Internet access (e-mail, Web surfing, including pages with audio and video), telephony (voice, video, fax, etc.), and multimedia (playing music, viewing videos, films, television, etc.) services through a single device.
Such services cannot be realized over 2G systems — to effect a simple transfer of a 2 MB presentation, it would take approximately 28 minutes with a 9.6 Kbps GSM data rate.

## Slide 5: 3G Standards
An evolution plan has been charted out to upgrade 2G technologies into their 3G counterparts.

## Slide 6: 3G Standards
In 1992, the International Telecommunications Union (ITU) initiated the standardization of 3G systems, and the outcome of this effort was called international mobile telecommunications-2000 (IMT-2000).
The number 2000 stood for three things:
  (i) the system would become available in the year 2000
  (ii) it has data rates of 2,000 Kbps
  (iii) it was supposed to operate in the 2,000 MHz region
which ITU wanted to make globally available for the new technology, so that users could roam seamlessly from country to country.
None of these three things came to pass, but the name has remained.
The service types that the IMT-2000 network is supposed to provide to its users are given in below table.

## Slide 7: IMT-2000 service types
As different parts of the world are dominated by different 2G standards, the hope for a single worldwide 3G standard has not materialized.

## Slide 8: 3G Standards
Universal mobile telecommunications system (UMTS) is the European 3G standard which is also called wideband CDMA (W-CDMA) as the standard is based on CDMA (direct sequence spread spectrum) technology.
The term “wideband” denotes use of a wide carrier.
W-CDMA uses a 5 MHz carrier (channel bandwidth) which is 25 times that of GSM and four times that of cdmaOne.
It is designed to interwork with GSM networks, which means a caller can move from a W-CDMA cell to a GSM cell without losing the call.
The first W-CDMA networks are being deployed in Japan by NTT DoCoMo.
Of the existing 2G systems, cdmaOne is already based on CDMA.
cdma2000, basically an extension of cdmaOne, is not designed to interwork with GSM, which means it cannot hand off calls to a GSM cell.
UWC-136 is a TDMA-based 3G standard developed by the Universal Wireless Communications Consortium, as an upgrade of IS-136.

## Slide 9: The Problems with 3G Systems
3G systems fundamentally need greater bandwidth and lower interference to be able to meet QoS requirements for data and multimedia services.
Field tests have indicated that CDMA is an attractive option for mobile cellular networks, as it can operate in the presence of interference, and can theoretically support very large bandwidth.
The performance of 3G systems is further improved by the use of smart antennas.
This refers to the technology of controlling a directional antenna array with an advanced digital signal processing capability to optimize its radiation and/or reception pattern automatically in response to the signal environment.

## Slide 10: The Problems with 3G Systems
3G systems promised to be the ultimate panacea to all problems of dropped calls, low data rates, and mobility restriction.
The initial time-chart had scheduled complete deployment of 3G by the year 2000. But this has really not happened.
The recommended spectrum allocation for 3G in the IMT-2000 could not be implemented as the requested frequencies by the ITU were partially or fully in use in many countries.
And it is becoming increasingly difficult to find a common slice of spectrum to enable global roaming.

## Slide 11: The Problems with 3G Systems
Another reason why 3G systems did not take off is the disappointing performance of CDMA in practice.
CDMA was projected to be the ultimate solution to interference.
Theoretically, an infinite number of users could use the same frequency band, since all of them hopped on all the frequencies in a pseudo-random sequence.
Below table shows the stark difference between the theoretical and practical performances of CDMA.

## Slide 12: CDMA — The debate

## Slide 13: The Problems with 3G Systems
It would be interesting to speculate where mobile telephony is heading at this point in time.
The first event on the agenda would be to implement 3G networks completely.
The trend seems to be headed toward having cells of different sizes: on the one hand, large cells to handle global access, and at the other extreme, pico-cells to handle indoor communication.

## Slide 14: The Problems with 3G Systems
Even though 3G networks are not yet fully deployed, some researchers started working on the next generation of systems, called 4G systems, targeted for deployment in the year 2010, to provide seamless integration with wired networks and especially IP, high bandwidth (data rates of up to 100 Mbps), ubiquity (connectivity everywhere), high-quality multimedia services, adaptive resource management, and software-defined radio.