## Slide 1: Wireless in Local Loop

## Slide 2: Wireless in Local Loop
  WLL Architecture
  WLL Technologies
  Broadband Wireless Access

## Slide 3: Wireless in Local Loop
Local loop is a circuit line from a subscriber’s phone to the local central office (LCO).
But the implementation of local loop of wires is risky for the operators, especially in rural and remote areas due to less number of users and increased cost of installation.
Hence, the solution for it is the usage of wireless local loop (WLL) which uses wireless links rather than copper wires to connect subscribers to the local central office.

## Slide 4: WLL Architecture
The architecture of a WLL system is similar to that of a mobile cellular system.
The BS is implemented by the base transceiver station system (BTS) and the base station controller (BSC).
The BTS, also called radio port (RP) or radio transceiver unit (RTU), performs channel coding, modulation/demodulation, and implements the radio interface for transmission and reception of radio signals.
A BSC, also called the radio port control unit (RPCU), controls one or more BTSs and provides them with an interface to the local exchange.

## Slide 5: WLL Architecture
The fixed subscriber unit (FSU) or radio subscriber unit (RSU) is the interface between the subscriber’s wired devices and the WLL network.
The FSU performs all physical and data-link layer functions from the subscriber end.
The basic architecture of WLL networks is shown in below figure.

## Slide 6: WLL Architecture

## Slide 7: WLL Technologies
WLL technology is at the intersection between cellular and cordless telephony.
Though there is no single global standard for WLL, many systems have been developed by suitable adaptation of cellular and cordless telephony standards.
  Cellular-Based WLL Systems(IS-95)
  Cordless-Based WLL Systems(DECT, PACS, PHS)
  Proprietary Systems(E-TDMA)
  Satellite-Based Systems(Iridium & Globalstar)
  Global Positioning System (GPS)

## Slide 8: Broadband Wireless Access
Fixed wireless systems are point-to-point (where a separate antenna transceiver is used for each user) or multipoint (where a single antenna transceiver is used to provide links to many users).
A multipoint system is similar to a conventional cellular system.
In a multipoint system
  cells do not overlap
  the same frequency is reused at each cell
  no handoff is provided as users are fixed
Two commonly used fixed wireless systems used for high-speed Internet access, are local multipoint distribution service (LMDS) and multichannel multipoint distribution service (MMDS).
These can be regarded as metropolitan area networks (MANs).

## Slide 9: LMDS
LMDS, operating at around 28 GHz in the United States and at around 40 GHz in Europe, is a broadband wireless technology used to provide voice, data, Internet, and video services.
Due to the high frequency at which LMDS systems operate, they are organized into smaller cells of 1-2 Km (against 45 Km in MMDS), which necessitates the use of a relatively large number of BSs in order to service a specific area.
LMDS systems offer very high data rates (maximum cell capacity of 155 Mbps).

## Slide 10: MMDS
MMDS operates at around 2.5 GHz in the licensed band and at 5.8 GHz in the unlicensed band in the United States, and LoS is required in most cases.
The lower frequencies (or larger wavelengths of MMDS signals) facilitate longer ranges of around 45 Km.
Due to the fact that equipment operating at low frequencies is less expensive, MMDS systems are also simpler and cheaper.
MMDS offer less bandwidth (the maximum capacity of an MMDS cell is 36 Mbps).
MMDS is also referred to as wireless cable as this service provides broadcast of TV channels in rural areas which are not reachable by broadcast TV or cable.