## Slide 1: IEEE 802.16 STANDARD
Wireless Inter-operability for Microwave Access (WiMAX)

## Slide 2: IEEE 802.16 STANDARD
Differences Between IEEE 802.11 and IEEE 802.16
Physical Layer
Data Link Layer

## Slide 3: IEEE 802.16 STANDARD
IEEE 802.16 specifies the air interface, including the data link layer (DLL) and the physical layer, of fixed point-to-multipoint broadband wireless access (BWA) systems.
The DLL is capable of supporting multiple physical layer specifications optimized for the frequency bands of the application.
Base stations (BSs) are connected to public networks.
A BS serves several subscriber stations (SSs), which in turn serve buildings.
The BS provides the SS with a last-mile (or first-mile) access to public networks.
Note - BSs and SSs are stationary.
The challenge faced by this standard was to provide support for multiple services with different QoS requirements and priorities simultaneously.

## Slide 4: IEEE 802.16 STANDARD

## Slide 5: Differences Between IEEE 802.11 and IEEE 802.16
While IEEE 802.11 has been a successful standard for WLANs, it is not suited for use in BWA.
IEEE 802.11 has been designed for mobile terminals, which is irrelevant in the context of MANs. IEEE 802.16 has been designed for broadband data such as digital video and telephony.
The number of users and bandwidth usage per user is much higher in a IEEE 802.16 network when compared to a typical IEEE 802.11 basic service set.
IEEE 802.16 is completely connection-oriented and QoS guarantees are made for all transmissions. IEEE 802.11 provides some QoS support for real-time data, it has not been designed for QoS support for broadband usage.

## Slide 6: Physical Layer
The physical layer uses traditional narrow-band radio (10-66 GHz) with conventional modulation schemes for transmission.
Above the physical transmission layer, there is a convergence sublayer to hide the transmission technology from the DLL.
Efforts are going on to add two new protocols, IEEE 802.16a and IEEE 802.16b, at the physical layer, which attempt to bring the IEEE 802.16 closer to IEEE 802.11.
While IEEE 802.16a operates in the 2-11 GHz frequency range, IEEE 802.16b operates in the 5 GHz ISM band.

## Slide 7: Physical Layer
The signal strength of millimeter waves falls off sharply with distance from the BS, which results in a reduction in the signal to noise ratio (SNR). To account for this, the following three modulation schemes are used.
The modulation scheme to be used is chosen depending on the distance of the SS from the BS.
  QAM-64, which offers 6 bits/baud, is used by subscribers that are located near the BS.
  QAM-16, which offers 4 bits/baud, is used by subscribers that are located at an intermediate distance from the BS.
  QPSK, which offers 2 bits/baud, is used by subscribers that are located far away from the BS.
If we assume 30 MHz of spectrum, QAM-64 offers 180 Mbps, QAM-16 offers 120 Mbps, and QPSK offers 60 Mbps.

## Slide 8: Data Link Layer
The DLL was designed with the wireless environment in which demands an efficient usage of the spectrum.
Broadband services call for very high uplink and downlink bit rates, and a range of QoS requirements.
Security issues also important in this scenario.
It is preferred that the DLL be a protocol-independent engine, i.e, the DLL should have convergence layers for all protocols including ATM, IP, and Ethernet.
The DLL of IEEE 802.16 was designed to meet all these requirements.
The DLL of IEEE 802.16 can be subdivided into three sublayers-
  Security sublayer
  MAC sublayer common part
  Service specific convergence sublayer

## Slide 9: Security sublayer
This is the bottom-most sublayer, which deals with privacy and security.
This is crucial for public outdoor networks where the transmission can be heard over a city.
This layer manages encryption, decryption, and key management.
In this only the payloads are encrypted, and the headers are kept intact.
This means that snooper can identify the participants in a transmission, but cannot read the data being transmitted.

## Slide 10: MAC sublayer common part
This is the protocol-independent core, which deals with channel management and slot allocation to stations.
Here the BS controls the system.
MAC frames are integral multiples of physical layer time slots.
Each frame contains the downstream (BS to SS) and upstream (SS to BS) maps, which indicate the traffic in the various time slots and other useful information.
The MAC sublayer strikes a trade-off between the stability of contention-less operation and the efficiency of contention-based operation, using a TDM/TDMA mechanism.
On the downlink, data to the SS is multiplexed using TDM, and on the uplink, the medium is shared by the SSs using TDMA.

## Slide 11: MAC sublayer common part
All services offered by IEEE 802.16 are connection-oriented, and each connection (uplink) is given one of the following four classes of service:
  Constant bit rate service
  Real-time variable bit rate service
  Non-real-time variable bit rate service
  Best effort service

## Slide 12: Constant bit rate service
This is intended for transmitting uncompressed voice, where a predetermined amount of data is generated at fixed time intervals.
Certain time slots are dedicated to each connection of this type and they are available automatically without explicit request.

## Slide 13: Real-time variable bit rate service
This is intended for compressed multimedia and soft real-time applications, where the amount of bandwidth required may vary with time.
To accommodate such variances, the BS polls the SS periodically to query the bandwidth needed for the following period.

## Slide 14: Non-real-time variable bit rate service
This is intended for large file transfers and other such heavy transmissions that are not real-time.
To accommodate them, the BS polls the SS often, but not periodically.

## Slide 15: Best effort service
All other applications contend for best effort service.
Polling is absent and SSs contend by sending requests for bandwidth in time slots marked in the upstream map as available for contention.
Collisions are reduced by using the binary exponential back-off algorithm.

## Slide 16: Service specific convergence sublayer
This is the topmost sublayer in DLL and its function is to interface to the network layer, which is similar to the logical link sublayer in other 802 protocols.
IEEE 802.16 has been designed to integrate seamlessly with both connection-less protocols such as PPP, IP, and Ethernet, and connection-oriented protocols such as ATM.
While mapping ATM connections to IEEE 802.16 is quite straightforward, mapping packets to IEEE 802.16 is done in a judicious manner by this sublayer.

## Slide 17: Service specific convergence sublayer
A request/grant scheme is used for handling bandwidth allocation.
Bandwidth requests are always per connection.
Bandwidth grants may be per connection (GPC) or per SS (GPSS).
Bandwidth GPSS is suitable if there are many connections per SS and this offloads the responsibilities of the BS.
SS redistributes bandwidth among its connections maintaining QoS and service level agreements.
While this method allows sophisticated QoS guarantees and a low overhead, it needs complex SSs.
Bandwidth GPC is suitable if there are only a few users per SS.
The BS grants bandwidth to each connection.
This incurs a higher overhead, but allows a simpler SS.