## Slide 1: HIPERACCESS
HIgh PErformance Radio ACCESS

## Slide 2: HIPERACCESS
Physical Layer
Convergence Layer
DLC Layer

## Slide 3: HIPERACCESS
The HIPERACCESS standard of the ETSI-BRAN (European Telecommunications Standards Institute – Broadband Radio Access Networks) pertains to broadband radio access systems and is the European counterpart to the IEEE 802.16 standard.
It uses fixed bidirectional radio connections to convey broadband services between users’ premises and a broadband core network.
HIPERACCESS systems are the means by which residential customers and small to medium-sized enterprises can gain access to broadband communications delivered to their premises by radio.
They provide support for a wide range of voice and data services and facilities.
They use radio to connect the premises to other users and networks, and offer “bandwidth on demand” to deliver the appropriate data rate needed for various services.

## Slide 4: HIPERACCESS
HIPERACCESS network deployments can potentially cover large areas.
A milliwave spectrum is employed in order to limit the transmission range to a few kilometers, owing to the large capacity requirements of the network.
A typical network consists of a number of cells each operating in a point-to-multipoint (PMP) manner; each cell consists of an access point (AP) equipment device located approximately at the cell center and a number of access termination (AT) devices which are spread across the cell.
The cell is divided into four sectors to increase the spectral efficiency by reusing the available radio frequency (RF) channels in a systematic manner within the deployment region.
The protocol stack of the HIPERACCESS standard consists of the physical layer, the convergence layer, and the data link control (DLC) layer.

## Slide 5: Physical Layer
The physical layer involves adaptive coding of the data obtained from the DLC layer, transmission of data, and support of the different duplex schemes, namely, frequency division duplexing (FDD), half-FDD (H-FDD), and time division duplexing (TDD).
The AP equipment handles more than one RF channel and more than one user (AT), hence its architecture is different from that of the AT.

## Slide 6: Convergence Layer
The task of the convergence layer is to adapt the service requirements of the applications of the higher layers to the services offered by the DLC layer.
There are two types of convergence layers - the cell-based convergence layer and the packet-based convergence layer.
The convergence layer is comprised of two parts - the service-independent common part (CP) and the service-specific convergence sublayer (SSCS).
This classification is similar to the data link layer of IEEE 802.16.

## Slide 7: DLC Layer
The basic features of the DLC layer are efficient use of the radio spectrum, high multiplex gain, and maintenance of QoS.
Multiplexing schemes are employed to make a better use of the available frequency spectrum at a lower equipment cost.
Unlike multiplexing, multiple access derives from the fact that every subscriber has access to every channel, instead of a fixed assignment as in most multiplex systems.

## Slide 8: DLC Layer
The DLC layer is connection-oriented to guarantee QoS.
Connections are set up over the air during the initialization of an AT, and additional new connections may be established when new services are required.

## Slide 9: Radio Link Control (RLC) Sublayer
The RLC sublayer performs functions pertaining to
  radio resource control
  initialization control
  connection control

## Slide 10: Radio resource control
This comprises all mechanisms for load-leveling, power-leveling, and change of physical modes.
These functions are specific to each AT.

## Slide 11: Initialization control
This includes functions for the initial access and release of a terminal to or from the network as well as the reinitialization process required in the case of link interruptions.
These mechanisms are AT specific.

## Slide 12: DLC connection control
This includes functions for the setup and release of connections and connection aggregates (groups of connections).
These functions are usually connection-specific.