## Slide 1: UNIT-III
PART-A
WIRELESS INTERNET

## Slide 2: SYLLABUS
What Is Wireless Internet?
Mobile IP
TCP In Wireless Domain
WAP
Optimizing Web Over Wireless

## Slide 3: What Is Wireless Internet?
Address Mobility
Inefficiency of Transport Layer Protocols
Inefficiency of Application Layer Protocols

## Slide 4: Introduction
Internet has caused a revolutionary change in the use of computers and search for information.
Wireless Internet enables the users to access information and data irrespective of their location.
Some protocols work well in wired network but perform very poor in the wireless networks such as TCP.

## Slide 5: What Is Wireless Internet?
Wireless Internet refers to the extension of the services offered by the Internet to mobile users, enabling them to access information and data irrespective of their location.
The inherent problems associated with wireless domain, mobility of nodes, and the design of existing protocols used in the Internet, require several solutions for making the wireless Internet a reality.
An illustration of wireless Internet with its layered protocol stack at wired and wireless parts is shown in below figure.
The major issues that are to be considered for wireless Internet are-
Address mobility
Inefficiency of transport layer protocols
Inefficiency of application layer protocols

## Slide 7: Address Mobility
The network layer protocol used in the Internet is Internet protocol (IP) which was designed for wired networks with fixed nodes.
IP employs a hierarchical addressing with a unique 32-bit address which has two parts, network identifier and host identifier, as shown in below figure.

## Slide 8: Address Mobility
The network identifier refers to the subnet address to which the host is connected.
This addressing scheme was used to reduce the routing table size in the core routers of the Internet, which uses only the network part of the IP address for making routing decisions.
This addressing scheme may not work directly in the wireless extension of the Internet, as the mobile hosts may move from one subnet to another, but the packets addressed to the mobile host may be delivered to the old subnet to which the node was originally attached, as illustrated in figures(b) and (c).

## Slide 9: Address Mobility

## Slide 10: Address Mobility
Hence the traditional IP addressing is not supportive of address mobility which is essential in wireless Internet.
Above figure shows the mobility of a node (with IP address 10.6.6.1) attached to subnet A (subnet address 10.6.6.x) moving over to another subnet B with address 10.6.15.x.
In this case, the packets addressed to the node will be routed to the subnet A instead of the subnet B, as the network part in the mobile node’s address is 10.6.6.x (see figure (c)).
MobileIP is a solution that uses an address redirection mechanism for this address mobility issue in wireless Internet.

## Slide 11: Inefficiency of Transport Layer Protocols
The transport layer is very important in the Internet as-
  it ensures setting up and maintaining end-to-end connections
  reliable end-to-end delivery of data packets
  flow control and congestion control.
TCP is the predominant transport layer protocol for wired networks, even though UDP, a connectionless unreliable transport layer protocol, is used by certain applications.
Wireless Internet requires efficient operation of the transport layer protocols as the wireless medium is inherently unreliable due to its time-varying and environment-dependent characteristics.
Traditional TCP invokes a congestion control algorithm in order to handle congestion in the networks.

## Slide 12: Inefficiency of Transport Layer Protocols
If a data packet or an ACK packet is lost, then TCP assumes that the loss is due to congestion and reduces the size of the congestion window by half.
With every successive packet loss the congestion window is reduced, and hence TCP provides a degraded performance in wireless links.
Even in situations where the packet loss is caused by link error or collision, the TCP invokes the congestion control algorithm leading to very low throughput.
The identification of the real cause that led to the packet loss is important in improving the performance of the TCP over wireless links.
Some of the solutions for the transport layer issues include indirect-TCP (ITCP), snoop TCP, and mobile TCP.

## Slide 13: Inefficiency of Application Layer Protocols
Traditional application layer protocols used in the Internet such as HTTP, TELNET, simple mail transfer protocol (SMTP), and several markup languages such as HTML were designed and optimized for wired networks.
Many of these protocols are not very efficient when used with wireless links.
The major issues that prevent HTTP from being used in wireless Internet are
  its stateless operation
  high overhead due to character encoding
  redundant information carried in the HTTP requests
  opening of a new TCP connection with every transaction

## Slide 14: Inefficiency of Application Layer Protocols
Wireless bandwidth is limited and much more expensive compared to wired networks.
Also, the capabilities of the handheld devices are limited, making it difficult to handle computationally and bandwidth-wise expensive application protocols.
Wireless application protocol (WAP) and optimizations over traditional HTTP are some of the solutions for the application layer issues.