## Slide 1: TCP In Wireless Domain

## Slide 2: TCP In Wireless Domain
Introduction
Traditional TCP
TCP Over Wireless
  Snoop TCP
  TCP-Unaware Link Layer
  Indirect TCP
  Mobile TCP
  Explicit Loss Notification
  WTCP
  TCP SACK
  Transaction-Oriented TCP
  Summary of the various approaches

## Slide 3: Introduction
The wireless domain is not only plagued by the mobility problem, but also by high error rates and low bandwidth.
Obviously there needs to be a higher layer abstraction that would perform the error recovery and flow control.
The traditional TCP, which guarantees in-order and reliable delivery, is the classical wired networks transmission protocol.
Since the transition to the wireless domain should be compatible with the existing infrastructure, there is need for modifications of the existing protocols.
This is the correct approach rather than resorting to a completely new set of protocols.

## Slide 4: Traditional TCP
TCP provides a connection-oriented, reliable, and byte stream service.
The term connection-oriented means the two applications using TCP must establish a TCP connection with each other before they can exchange data.
It is a full duplex protocol, meaning that each TCP connection supports a pair of byte streams, one flowing in each direction.
TCP includes a flow-control mechanism for each of these byte streams that allows the receiver to limit how much data the sender can transmit.
TCP also implements a congestion-control mechanism.
TCP divides the data stream to be sent into smaller segments and assigns sequence numbers to them.
The sequence number helps the receiver to provide the higher layers with in-order packet delivery, and also detect losses.

## Slide 5: Traditional TCP
The sliding window mechanism employed by TCP guarantees the reliable delivery of data, ensures that the data is delivered in order, and enforces flow control between the sender and the receiver.
In the sliding-window process, the sender sends several packets before awaiting acknowledgment of any of them, and the receiver acknowledges several packets at a time by sending to the transmitter the relative byte position of the last byte of the message that it has received successfully.
The number of packets to be sent before the wait for acknowledgment (window size) is set dynamically, that is, it can change from time to time depending on network conditions.

## Slide 6: Traditional TCP
Because the major cause of packet loss in the wired domain is congestion, TCP assumes that any loss is due to congestion.
The TCP congestion control mechanism works as below.
Initially, the TCP sender sets the congestion window to the size of one maximum TCP segment [also known as maximum segment size (MSS)].
The congestion window gets doubled for each successful transmission of the current window.
This process continues until the size of the congestion window exceeds the size of the receiver window or the TCP sender notices a timeout for any TCP segment.

## Slide 7: Traditional TCP
The TCP sender interprets the timeout event as network congestion, initializes a parameter called slow start threshold to half the current congestion window size, and resets the congestion window size to one MSS.
It then continues to double the congestion window on every successful transmission and repeats the process until the congestion window size reaches the slow start window threshold.
Once the threshold is reached, the TCP sender increases the congestion window size by one MSS for each successful transmission of the window.
This mechanism whereby the congestion window size is brought down to one MSS each time network congestion is detected and then is incremented as described above is referred to as slow start.

## Slide 8: Traditional TCP
Another important characteristic of TCP is fast retransmit and recovery.
If the receiver receives packets out of order, it continues to send the acknowledgment for the last packet received in sequence.
This indicates to the sender that some intermediate packet was lost and the sender need not invoke the congestion control mechanism.
The sender then reduces the window size by half and retransmits the missing packet.
This avoids the slow start phase.

## Slide 9: Traditional TCP

## Slide 10: Traditional TCP
Congestion Control Mechanism - Initial Window size: Max segment size - Window get doubled for each successful transmission -TCP interpret Timeout as congestion -> initialize Slow Start Threshold as half of current window and reset window as one Max segment size

## Slide 11: TCP Over Wireless
The adaptation of TCP to congestion causes a lot of problems in the wireless domain.
The wireless domain has high packet loss and variable latency, which may cause TCP to respond with slow start.
Bandwidth utilization is further reduced due to retransmission of lost packets.
There are several alternatives for improving the performance of TCP over wireless networks was to ensure that the link layer corrected all the errors itself over the wireless interface, thereby eliminating the need for error handling at the TCP layer.

## Slide 12: TCP Over Wireless
One of the technique in this category is the use of forward error correction (FEC) to correct small errors.
FEC is a means of error control coding wherein redundancy is encoded into the sent message or binary stream to allow self-correction at the receiver.
The main objective of these techniques is to hide errors from TCP as far as possible.
However, FEC incurs overhead even when there are no errors as there must be the redundant parity bits to allow error detection and correction.

## Slide 13: TCP Over Wireless
The other form of link layer recovery is to use retransmissions at the link layer.
This incurs the overhead only on error.
However, the link level recovery mechanism may cause head-of-the-line blocking, wherein the recovery mechanisms employed for one data stream consume the network resources and prevent others from being able to transmit packets.

## Slide 14: TCP Over Wireless
Several alternatives have been proposed to alter the existing TCP protocol to suit the wireless domain.
The simplest idea would be to design a new TCP protocol for the wireless domain, but this will be incompatible with the wired domain.

## Slide 15: Snoop TCP
The idea used in snoop TCP is to buffer the data as close to MN as possible to minimize the time for retransmission.
The BS just snoops the packets being transmitted in both directions and recognizes the acknowledgments.
If BS gets a duplicate acknowledgment (DUPACK) or no acknowledgment for quite some time, then it retransmits from the buffer after discarding the duplicate acknowledgment.
When the data transmission is from MN to CN, if the BS detects a gap in the sequence numbers acknowledged by the CN, it sends a NACK or negative acknowledgment to the MN to indicate loss over the wireless link.

## Slide 16: TCP-Unaware Link Layer
This strategy particularly aims at simulating the behavior of the snoop-TCP protocol without requiring the link layer at the BS to be TCP-aware.
The usage of delayed DUPACKs imitates snoop-TCP without requiring the link layer at BS to be TCP-aware.
At the BS, as in snoop-TCP, link layer retransmission is used to perform local error recovery.
But unlike snoop-TCP, where retransmissions are triggered by TCP DUPACKs, here retransmissions are triggered by link level ACKs.
The MN reduces the interaction between the link layer and TCP using delayed DUPACKs.

## Slide 17: TCP-Unaware Link Layer
The advantages of this scheme are that the link layer need not be TCP-aware, it can be used even if headers are encrypted, which is not possible in snoop-TCP, which needs to look into the headers to see the sequence numbers, and it works well for small round trip times (RTTs) over the wireless link.
The most significant disadvantage of this mechanism is that the optimum value of DUPACK delay is dependent on the wireless link, and this value is crucial in determining the performance.

## Slide 18: Indirect TCP
This approach involves splitting of the TCP connection into two distinct connections, one TCP connection between the MN and BS and another TCP connection between the BS and the CN.
In this case, the intermediate agent commonly known as the access point (AP) acts as a proxy for MN.
The AP acknowledges CN for the data sent to MN and buffers this data until it is successfully transmitted to MN.
MN acknowledges the AP alone for the data received.

## Slide 19: Indirect TCP

## Slide 20: Mobile TCP
The most common problem associated with the wireless domain is that quite often the connection between MN and BS is lost for small intervals of time.
This typically happens when MN moves behind a huge building or MN enters offices where the signals are filtered.
In such situations the sender needs to be informed.
This situation is handled in mobile TCP (M-TCP) by the supervisory host which advertises the window size to be one, thus choking the sender and hence avoiding slow start.
Connection may be resumed when MN can be contacted again.

## Slide 21: Mobile TCP
When the supervisory host receives a TCP packet, it forwards it to the M-TCP client.
Upon reception of an ACK from MTCP client, the supervisory host forwards the ACK to the TCP sender.
Hence M-TCP maintains the end-to-end TCP semantics even though the TCP connection is split at the supervisory host.
When the M-TCP client undergoes a temporary link break, the supervisory host avoids forwarding the ACK of the last byte to the sender and hence the sender TCP goes to the persist state by setting the window size to zero.
This avoids retransmission, closing of the congestion window, and slow start at the sender.

## Slide 22: Explicit Loss Notification
TCP does not know the exact cause for packet loss, and hence has to invariably assume congestion loss.
An ideal TCP simply retransmits the lost packets without any congestion control mechanism.
The MAC layer can identify the reason for the packet loss.
Once the MAC layer detects that either a handoff is about to occur or realizes that the actual cause of the packet loss is not congestion, then it immediately informs the TCP layer of the possibility of a non-congestion loss.
The crux of the strategy is to detect loss at MN and send an explicit loss notification (ELN) to the sender.
The sender does not reduce window size on receiving the ELN as this message implies that there was an error and not congestion.

## Slide 23: WTCP
WTCP aims at revamping the transport protocol for the wireless domain using
  rate-based transmission at the source
  inter-packet separation at the receiver as the congestion metric
  mechanisms for detecting the reason for packet loss
  bandwidth estimation

## Slide 24: WTCP
A unique characteristic of WTCP is the attempt to separate the congestion control and reliability mechanisms.
WTCP uses separate sequence numbers for congestion control and reliability mechanisms in order to distinguish the two.
The reliability mechanism involves a combination of selective and cumulative acknowledgments, and takes into account the reverse-path characteristics for determining the ACK frequency.

## Slide 25: TCP SACK
The selective retransmission strategy is more complex and requires more buffer space at the end-points.
Hence TCP traditionally uses cumulative acknowledgments and the go-back-N strategy.
Using selective retransmit reduces the overhead of retransmission on errors and therefore cannot be ruled out for use in wireless domains.
The TCP with selective ACK scheme (TCP SACK) improves TCP performance by allowing the TCP sender to retransmit packets based on the selective ACKs provided by the receiver.

## Slide 26: Transaction-Oriented TCP
The TCP connection setup and connection tear-down phases involve a huge overhead in terms of time and also in terms of the number of packets sent.
This overhead is very costly, especially if the size of the data is small.
An alternative for such transactions is transaction-oriented TCP (TTCP).
The motivation behind this approach is to integrate the call setup, the call tear-down, and the actual data transfer into a single transaction, thereby avoiding separate packets for connecting and disconnecting.

## Slide 27: Summary of the various approaches