## Slide 1: WAP
Wireless Application Protocol

## Slide 2: WAP
Introduction
The WAP Model
The WAP Protocol Stack

## Slide 3: Introduction
WAP represents a suite of protocols rather than a single protocol.
WAP has today become the de facto standard for providing data and voice services to wireless handheld devices.
WAP aims at integrating a simple lightweight browser also known as a micro-browser into handheld devices, thus requiring minimal amounts of resources such as memory and CPU at these devices.

## Slide 4: Introduction
Main objectives of the WAP protocol suite are independence from the wireless network standards, interoperability among service providers, overcoming the shortfalls of the wireless medium (such as low bandwidth, high latency, low connection stability, and high transmission cost per bit), overcoming the drawbacks of handheld devices (small display, low memory, limited battery power, and limited CPU power), increasing efficiency and reliability, and providing security, scalability, and extensibility.

## Slide 5: The WAP Model
The WAP model consists of 3 levels known as Client, Gateway and Origin Server.
When a user opens the browser in his/her mobile device and selects a website that he/she wants to view, the mobile device sends the URL encoded request via a network to a WAP gateway using WAP protocol.
The request he/she sends via mobile to WAP gateway is called as encoding request.
The sent encoding request is translated through WAP gateway and then forwarded in the form of a conventional HTTP URL request over the Internet.
When the request reaches a specified Web server, the server processes the request just as it would handle any other request and sends the response back to the mobile device through WAP gateway.
Now, the WML file's final response can be seen in the browser of the mobile users.

## Slide 6: The WAP Model

## Slide 7: The WAP Protocol Stack
It specifies the different communications and data transmission layers used in the WAP model:

## Slide 8: 1. Application Layer
This layer contains the Wireless Application Environment (WAE).
It contains mobile device specifications and content development programming languages like WML.

## Slide 9: 2. Session Layer
This layer contains Wireless Session Protocol (WSP).
It provides fast connection suspension and reconnection.

## Slide 10: 3. Transaction Layer
This layer contains Wireless Transaction Protocol (WTP).
It runs on top of UDP (User Datagram Protocol) and is a part of TCP/IP and offers transaction support.

## Slide 11: 4. Security Layer
This layer contains Wireless Transaction Layer Security (WTLS).
It offers data integrity, privacy and authentication.

## Slide 12: 5. Transport Layer
This layer contains Wireless Datagram Protocol.
It presents consistent data format to higher layers of WAP protocol stack.