## Slide 1: Issues in Ad Hoc Wireless Networks

## Slide 2: Issues in Ad Hoc Wireless Networks
Medium access scheme
Routing
Multicasting
Transport layer protocol
Pricing scheme
Quality of service provisioning
Self-organization
Security
Addressing and service discovery
Energy management
Scalability
Deployment considerations

## Slide 3: Medium access scheme
The primary responsibility of a medium access control (MAC) protocol in ad hoc wireless networks is the distributed arbitration for the shared channel for transmission of packets.
The performance of any wireless network hinges on the MAC protocol, more so for ad hoc wireless networks.

## Slide 4: Medium access scheme
The major issues to be considered in designing a MAC protocol for ad hoc wireless networks are as follows:
Distributed operation
Synchronization
Hidden terminals
Exposed terminals
Throughput
Access delay
Fairness
Real-time traffic support
Resource reservation
Ability to measure resource availability
Capability for power control
Adaptive rate control
Use of directional antennas

## Slide 5: Routing
The responsibilities of a routing protocol include
  Exchanging the route information
  Finding a feasible path to a destination based on criteria such as hop length, minimum power required, and lifetime of the wireless link
  Gathering information about the path breaks
  Mending the broken paths expending minimum processing power and bandwidth
  Utilizing minimum bandwidth

## Slide 6: Routing
The major challenges that a routing protocol faces are as follows:
  Mobility
  Bandwidth constraint
  Error-prone and shared channel
  Location-dependent contention
  Other resource constraints

## Slide 7: Routing
The major requirements of a routing protocol in ad hoc wireless networks are the following:
  Minimum route acquisition delay
  Quick route reconfiguration
  Loop-free routing
  Distributed routing approach
  Minimum control overhead
  Scalability
  Provisioning of QoS
  Support for time-sensitive traffic
  Security and privacy

## Slide 8: Multicasting
Multicasting plays an important role in the typical applications of ad hoc wireless networks, namely, emergency search-and-rescue operations and military communication.
In such an environment, nodes form groups to carry out certain tasks that require point-to-multipoint and multipoint-to-multipoint voice and data communication.
The arbitrary movement of nodes changes the topology dynamically in an unpredictable manner.
The mobility of nodes, with the constraints of power source and bandwidth, makes multicast routing very challenging.

## Slide 9: Multicasting
The major issues in designing multicast routing protocols are as follows:
  Robustness
  Efficiency
  Control overhead
  Quality of service
  Efficient group management
  Scalability
  Security

## Slide 10: Transport layer protocol
The main objectives of the transport layer protocols include setting up and maintaining end-to-end connections, reliable end-to-end delivery of data packets, flow control, and congestion control.
There exist simple connectionless transport layer protocols (e.g., UDP) which neither perform flow control and congestion control nor provide reliable data transfer.
Such unreliable connectionless transport layer protocols do not take into account the current network status such as congestion at the intermediate links, the rate of collision, or other similar factors affecting the network throughput.
This behavior of the transport layer protocols increases the contention of the already-choked wireless links.
The major performance degradation faced by a reliable connection-oriented transport layer protocol such as transmission control protocol (TCP) in an ad hoc wireless network arises due to frequent path breaks, presence of stale routing information, high channel error rate, and frequent network partitions.

## Slide 11: Pricing scheme
An ad hoc wireless network’s functioning depends on the presence of relaying nodes and their willingness to relay other nodes’ traffic.
Even if the node density is sufficient enough to ensure a fully connected network, a relaying neighbor node may not be interested in relaying a call and may just decide to power down.
The obvious solution to provide participation guarantee is to provide incentives to forwarding nodes.

## Slide 12: Quality of service provisioning
Quality of service (QoS) is the performance level of services offered by a service provider or a network to the user.
QoS provisioning often requires negotiation between the host and the network, resource reservation schemes, priority scheduling, and call admission control.
Rendering QoS in ad hoc wireless networks can be on a per flow, per link, or per node basis.
In ad hoc wireless networks, the boundary between the service provider (network) and the user (host) is blurred, thus making it essential to have better coordination among the hosts to achieve QoS.
The lack of central coordination and limited resources exacerbate the problem.

## Slide 13: Self-organization
One very important property that an ad hoc wireless network should exhibit is organizing and maintaining the network by itself.
The major activities that an ad hoc wireless network is required to perform for self-organization are -
  neighbor discovery
  topology organization
  topology reorganization

## Slide 14: Security
The security of communication in ad hoc wireless networks is very important, especially in military applications.
The lack of any central coordination and shared wireless medium makes them more vulnerable to attacks than wired networks.
The attacks against ad hoc wireless networks are generally classified into two types: passive and active attacks.
Passive attacks refer to the attempts made by malicious nodes to perceive the nature of activities and to obtain information transacted in the network without disrupting the operation.
Active attacks disrupt the operation of the network.
Those active attacks that are executed by nodes outside the network are called external attacks, and those that are performed by nodes belonging to the same network are called internal attacks.
Nodes that perform internal attacks are compromised nodes.

## Slide 15: Security
The major security threats that exist in ad hoc wireless networks are as follows:
  Denial of service
  Resource consumption
    Energy depletion
    Buffer overflow
  Host impersonation
  Information disclosure
  Interference

## Slide 16: Addressing and service discovery
Addressing and service discovery assume significance in ad hoc wireless networks due to the absence of any centralized coordinator.
An address that is globally unique in the connected part of the ad hoc wireless network is required for a node in order to participate in communication.
Auto-configuration of addresses is required to allocate non-duplicate addresses to the nodes.
In networks where the topology is highly dynamic, frequent partitioning and merging of network components require duplicate address-detection mechanisms in order to maintain unique addressing throughout the connected parts of the network.
Nodes in the network should be able to locate services that other nodes provide.
Hence efficient service advertisement mechanisms are necessary.

## Slide 17: Energy management
Energy management is defined as the process of managing the sources and consumers of energy in a node or in the network as a whole for enhancing the lifetime of the network.
Some of the functions of energy management are -
  Shaping the energy discharge pattern of a node’s battery to enhance the battery life
  finding routes that result in minimum total energy consumption in the network
  using distributed scheduling schemes to improve battery life
  handling the processor and interface devices to minimize power consumption

## Slide 18: Energy management
Energy management can be classified into the following categories:
  Transmission power management
  Battery energy management
  Processor power management
  Devices power management

## Slide 19: Scalability
Even though the number of nodes in an ad hoc wireless network does not grow in the same magnitude as today’s Internet, the operation of a large number of nodes in the ad hoc mode is not far away.
Traditional applications such as military, emergency operations, and crowd control may not lead to such a big ad hoc wireless network.
Commercial deployments of ad hoc wireless networks that include wireless mesh networks show early trends for a widespread installation of ad hoc wireless networks for mainstream wireless communication.
A hierarchical topology-based system and addressing may be more suitable for large ad hoc wireless networks.
Hybrid architectures that combine the multi-hop radio relaying in the presence of infrastructure may improve scalability.

## Slide 20: Deployment considerations
The deployment of ad hoc wireless networks involves actions different from those of wired networks.
It requires a good amount of planning and estimation of future traffic growth over any link in the network.
The time-consuming planning stage is followed by the actual deployment of the network.
The cost and time required for laying copper cables or fiber cables make it difficult to reconfigure any partial deployment that has already been done.
The deployment of a commercial ad hoc wireless network has the following benefits when compared to wired networks:

## Slide 21: Deployment considerations
The deployment of a commercial ad hoc wireless network has the following benefits when compared to wired networks:
  Low cost of deployment
  Incremental deployment
  Short deployment time
  Reconfigurability
  Scenario of deployment
  Required longevity of network
  Area of coverage
  Service availability
  Operational integration with other infrastructure
  Choice of protocols