## Slide 1: Ad Hoc Wireless Internet

## Slide 2: Ad Hoc Wireless Internet
Ad hoc wireless Internet extends the services of the Internet to the end users over an ad hoc wireless network.
Some of the applications of the ad hoc wireless Internet are
  wireless mesh networks
  provisioning of temporary Internet services to major conference venues
  sports venues
  temporary military settlements
  battlefields
  broadband Internet services in rural regions
A schematic diagram of the ad hoc wireless Internet is shown in below figure.

## Slide 3: Ad Hoc Wireless Internet

## Slide 4: Ad Hoc Wireless Internet
The major issues to be considered for a successful ad hoc wireless Internet are the following:
Gateways
Address mobility
Routing
Transport layer protocol
Load balancing
Pricing/billing
Provisioning of security
QoS support
Service, address, and location discovery

## Slide 5: Gateways
There are the entry points to the wired Internet.
Generally owned and operated by a service provider.
Gateways perform the following tasks:
  keeping track of the end users
  Bandwidth management
  load balancing
  traffic shaping
  packet filtering
  Bandwidth fairness
  address, service, and location discovery

## Slide 6: Address mobility
The ad hoc wireless Internet also faces the challenge of address mobility.
This problem is worse here as the nodes operate over multiple wireless hops.
Solutions such as Mobile IP can provide temporary alternatives for this.

## Slide 7: Routing
It is a major problem in the ad hoc wireless Internet, due to dynamic topological changes, the presence of gateways, multi-hop relaying, and the hybrid character of the network.
Possible solution is to use separate routing protocol, for the wireless part of the ad hoc wireless Internet.

## Slide 8: Transport layer protocol
Even though several solutions for transport layer protocols exist for ad hoc wireless networks, unlike other layers, the choice lies in favor of TCP’s extensions proposed for ad hoc wireless networks.
Split approaches that use traditional wired TCP for the wired part and a specialized transport layer protocol for the ad hoc wireless network part can also be considered where the gateways act as the intermediate nodes at which the connections are split.
Several factors are to be considered here, the major one being the state maintenance overhead at the gateway nodes.

## Slide 9: Load balancing
It is likely that the ad hoc wireless Internet gateways experience heavy traffic.
Hence the gateways can be saturated much earlier than other nodes in the network.
Load balancing techniques are essential to distribute the load so as to avoid the situation where the gateway nodes become bottleneck nodes.

## Slide 10: Pricing/billing
Since Internet bandwidth is expensive, it becomes very important to introduce pricing/billing strategies for the ad hoc wireless Internet.
Gateway is the preferred choice for charging the traffic to and from the Internet.
A much more complex case is pricing the local traffic, where it becomes necessary to have a dedicated, secure, and lightweight pricing/billing infrastructure installed at every node.

## Slide 11: Provisioning of security
The inherent broadcast nature of the wireless medium attracts not just the mobility seekers but also potential hackers who love to snoop on important information sent unprotected over the air.
Hence security is a prime concern in the ad hoc wireless Internet.
Since the end users can utilize the ad hoc wireless Internet infrastructure to make e-commerce transactions, it is important to include security mechanisms in the ad hoc wireless Internet.

## Slide 12: QoS support
With the widespread use of voice over IP (VoIP) and growing multimedia applications over the Internet, provisioning of QoS support in the ad hoc wireless Internet becomes a very important issue.

## Slide 13: Service, address, and location discovery
Service discovery refers to the activity of discovering or identifying the party which provides a particular service or resource.
Address discovery refers to the services such as those provided by address resolution protocol (ARP) or domain name service (DNS) operating within the wireless domain.
Location discovery refers to different activities such as detecting the location of a particular mobile node in the network or detecting the geographical location of nodes.
Location discovery services can provide enhanced services such as routing of packets, location-based services, and selective region-wide broadcasts.