## Slide 1: WIRELESS AD-HOC NETWORKS
UNIT-I
SYLLABUS

## Slide 2: INTRODUCTION
Radio Propagation Mechanisms
Characteristics of the Wireless Channel
Modulation Techniques
Multiple Access Techniques
Voice Coding
Computer Network Architecture
IEEE 802 Networking Standards
Wireless Network

## Slide 3: INTRODUCTION
Radio Propagation Mechanisms
Characteristics of the Wireless Channel
Modulation Techniques
Multiple Access Techniques
Voice Coding
Computer Network Architecture
IEEE 802 Networking Standards
Wireless Network

## Slide 4: Radio Propagation Mechanisms
Radio waves generally experience the following three propagation mechanisms:
Reflection
Diffraction
Scattering

## Slide 5: 1. Reflection
When the propagating radio wave hits an object which is very large compared to its wavelength (such as the surface of the Earth, or tall buildings), the wave gets reflected by that object.
Reflection causes a phase shift of 180 degrees between the incident and the reflected rays.

## Slide 6: 2. Diffraction
This propagation effect is undergone by a wave when it hits an impenetrable object.
The wave bends at the edges of the object, thereby propagating in different directions.
This phenomenon is termed as diffraction.
The dimensions of the object causing diffraction are comparable to the wavelength of the wave being diffracted.
The bending causes the wave to reach places behind the object which generally cannot be reached by the line-of-sight transmission.
The amount of diffraction is frequency-dependent, with the lower frequency waves diffracting more.

## Slide 7: 3. Scattering
When the wave travels through a medium, which contains many objects with dimensions small when compared to its wavelength, scattering occurs.
The wave gets scattered into several weaker outgoing signals.
In practice, objects such as street signs, lamp posts, and foliage cause scattering.

## Slide 8
Figure 1.1. Radio propagation mechanisms

## Slide 9: Radio Propagation Mechanisms
Figure 1.1 depicts the various propagation mechanisms that a radio wave encounters.
When the transmitted wave is received at the receiver, the received power of the signal is generally lower than the power at which it was transmitted.
The loss in signal strength, known as attenuation, is due to several factors.