## Slide 1: Characteristics of the Wireless Channel

## Slide 2: Characteristics of the Wireless Channel
The various characteristics of the wireless are –
Path loss
Fading
Interference
Doppler shift

## Slide 3: 1. Path loss
Path loss can be expressed as the ratio of the power of the transmitted signal to the power of the same signal received by the receiver, on a given path.
It is a function of the propagation distance.
Estimation of path loss is very important for designing and deploying wireless communication networks.
Path loss is dependent on a number of factors such as the radio frequency used and the nature of the terrain.

## Slide 4: 1. Path loss
In designing a network, several models are required to describe the variety of transmission environments.
Free space propagation model
Two-ray model or Two-path model

## Slide 6: Free space propagation model
The free space propagation model is the simplest path loss model in which there is a direct-path signal between the transmitter and the receiver, with no atmospheric attenuation or multipath components.
In this model the relationship between the transmitted power Pt and the received power Pr is given by

## Slide 7: Free space propagation model
Where Gt and Gr are the transmitter and receiver antenna gains, d is the distance between the transmitter and receiver, and λ = c / f is the wavelength of the signal.
Where c is the speed of light (3 × 10^8 m/s), f is the frequency of the wave in Hz, and λ is its wavelength in meters.

## Slide 8: Two-ray model or Two-path model
The free space model described above assumes that there is only one single path from the transmitter to the receiver.
But in reality, the signal reaches the receiver through multiple paths (because of reflection, refraction, and scattering).
The two-path model tries to capture this phenomenon.
The model assumes that the signal reaches the receiver through two paths, one a line-of-sight path, and the other the path through which the reflected (or refracted, or scattered) wave is received.

## Slide 9: Two-ray model or Two-path model
According to the two-path model, the received power is given by
Where Pt is the transmitted power, Gt and Gr represent the antenna gains at the transmitter and the receiver, d is the distance between the transmitter and receiver, and ht and hr are the heights of the transmitter and the receiver.

## Slide 10: 2. Fading
Fading refers to the fluctuations in signal strength when received at the receiver. Fading can be classified into two types:
Fast fading / Small-scale fading
Slow fading / Large-scale fading

## Slide 11: Fast Fading
Fast fading refers to the rapid fluctuations in the amplitude, phase, or multipath delays of the received signal, due to the interference between multiple versions of the same transmitted signal arriving at the receiver at slightly different times.
The time between the reception of the first version of the signal and the last echoed signal is called delay spread.

## Slide 12: Slow Fading
The name Slow Fading itself implies that the signal fades away slowly.
Slow fading occurs when objects that partially absorb the transmissions lie between the transmitter and receiver.
Slow fading is so called because the duration of the fade may last for multiple seconds or minutes.
Slow fading may occur when the receiver is inside a building and the radio wave must pass through the walls of a building, or when the receiver is temporarily shielded from the transmitter by a building.
Slow fading is also referred to as shadow fading since the objects that cause the fade, which may be large buildings or other structures, block the direct transmission path from the transmitter to the receiver.

## Slide 13: 3. Interference
Wireless transmissions have to counter interference from a wide variety of sources.
Two main forms of interference are-
Adjacent channel interference
Co-channel interference

## Slide 14: Adjacent channel interference
In the adjacent channel interference case, signals in nearby frequencies have components outside their allocated ranges, and these components may interfere with on-going transmissions in the adjacent frequencies.
It can be avoided by carefully introducing guard bands between the allocated frequency ranges.

## Slide 15: Co-channel interference
Co-channel interference, sometimes also referred to as narrow-band interference, is due to other nearby systems using the same transmission frequency.

## Slide 16: 4. Doppler Shift
The Doppler shift is defined as the change/shift in the frequency of the received signal when the transmitter and the receiver are mobile with respect to each other.
If they are moving toward each other, then the frequency of the received signal will be higher than that of the transmitted signal, and if they are moving away from each other, the frequency of the signal at the receiver will be lower than that at the transmitter.
The Doppler shift fd is given by fd = v/λ
Where v is the relative velocity between the transmitter and receiver, and λ is the wavelength of the signal.

## Slide 17: Transmission Rate Constraints
Two important constraints that determine the maximum rate of data transmission on a channel are-
Nyquist’s theorem
Shannon’s theorem

## Slide 18: Nyquist’s theorem
The Nyquist theorem gives the maximum data rate possible on a channel.
If B is the bandwidth of the channel (in Hz) and L is the number of discrete signal levels/voltage values used, then the maximum channel capacity C according to the Nyquist theorem is given by
C = 2×B×log2L bits/sec
The above condition is valid only for a noiseless channel.

## Slide 19: Shannon’s Theorem
Noise level in the channel is represented by the SNR.
It is the ratio of signal power (S) to noise power (N), specified in decibels, that is, SNR = 10 log10(S/N).
The most important contributions of Shannon was his theorem on the maximum data rate possible on a noisy channel.
According to Shannon’s theorem, the maximum data rate C is given by
C = B×log2(1 + (S/N)) bits/sec
Where B is the bandwidth of the channel (in Hz).