## Slide 1: Modulation Techniques

## Slide 2: Modulation Techniques
In this technique we see how raw bits constituting the information are actually transmitted on the wireless medium.
Data (whether in analog or in digital format) has to be converted into electromagnetic waves for transmission over a wireless channel.
The techniques that are used to perform this conversion are called modulation techniques.
The modulation process alters certain properties of a radio wave, called a carrier wave, whose frequency is the same as the frequency of the wireless channel being used for the transmission.
The modulation scheme to be used must be chosen carefully so that the limited radio spectrum is used efficiently.
Modulation schemes can be classified under two major categories-
Analog modulation schemes
Digital modulation schemes
This classification is based on the nature of the data, analog or digital, to be transmitted.

## Slide 3: 1. Analog Modulation
As the name implies, analog modulation techniques are used for transmitting analog data.
The analog data signal is superimposed on a carrier signal.
This superimposition is aimed at altering a certain property (amplitude or frequency) of the carrier signal.
Some of the commonly used analog modulation techniques are-
Amplitude modulation
Frequency modulation
Phase modulation

## Slide 4: Amplitude modulation
It was the first method to be used for transmitting voice.
The transmitter superimposes the information signal x(t), also called the modulating signal, on the carrier signal c(t).
The result of AM of the carrier signal of Figure 1.2 (b), by the information/ modulating signal of Figure 1.2 (a), is shown in Figure 1.2 (c).

## Slide 5
Figure 1.2. Analog modulation schemes
H=A
W=F

## Slide 6: Amplitude modulation
It can be seen that the frequency of the modulated wave remains constant, while its amplitude varies with that of the information signal.
As the power of a signal depends on its amplitude, the power of the transmitted wave depends on the power of the modulating signal.

## Slide 7: Amplitude modulation
When a cosine carrier wave is used, the AM wave can be mathematically represented as below:
s(t) = (1+nax(t)) cos(2πfct)
Where na, known as the modulation index, is the ratio of the amplitude of the information signal to that of the carrier signal, fc is the frequency of the carrier signal, x(t) is the information signal, and c(t) = cos(2πfct) is the carrier signal.

## Slide 8: Amplitude modulation
In modern communication systems, AM is not the preferred modulation mechanism.
AM creates additional unwanted signals in frequencies on either side of the carrier during the superimposition process.
These signals, called sidebands, lead to poor spectrum utilization, and they consume additional power.
Hence, AM is considered to be an inefficient modulation mechanism.
A variant of AM, where the sidebands are stripped away on one side, called single side band (SSB), is often used in place of plain AM.
Broadcast radio is one of the applications which still uses AM.

## Slide 9: Angle Modulation
Frequency modulation and phase modulation come under this category.
The angle modulated signal can be mathematically represented as
s(t) = Ac[cos(2πfct) +Φ(t)]
where Ac is the amplitude and fc is the frequency of the carrier signal.
Frequency modulation and phase modulation are special cases of angle modulation.
Changing the frequency of a wave also changes its phase, and vice versa.
The angle modulated signal has a constant amplitude, and as a consequence the transmitter operates at full power constantly, which also maximizes its range.

## Slide 10: Frequency Modulation
In frequency modulation (FM), the amplitude of the modulated signal is kept constant, while the instantaneous frequency is altered to reflect the information signal that is being transmitted.
Frequency modulation follows Equation AM with the condition that the derivative of the phase, that is, Φ`(t), is proportional to the information signal x(t).
Since frequency can also be defined as the rate of change of phase of the signal, here Φ`(t) represents the deviation of the instantaneous frequency of the modulated signal from that of the carrier signal.

## Slide 11: Frequency Modulation
In FM, this Φ`(t) is directly proportional to the information signal/modulating signal. It can be represented as Φ`(t) = nfx(t)
Where nf is a constant, known as the frequency modulation index.
Below figure shows the FM modulated signal.

## Slide 13: Phase Modulation
In phase modulation (PM), the phase of the modulated signal Φ(t) is directly proportional to the information signal x(t).
It is represented as Φ(t) = npx(t)
where np is a constant, known as the phase modulation index.
It can be seen from Equation AM that [2πfct+Φ(t)] is the phase of the modulated signal.
The instantaneous phase deviation of the modulated signal from the carrier signal is Φ(t).
In PM, this Φ(t) is proportional to the information signal/modulating signal.

## Slide 14: 2. Digital Modulation
Digital modulation schemes are used for transmitting digital signals that consist of a sequence of 0 and 1 bits.
As in analog modulation, digital modulation also changes a certain property of the carrier signal.
The main difference between analog and digital modulation is that while the changes occur in a continuous manner in analog modulation, they occur at discrete time intervals in digital modulation.
The number of such changes per second is known as the baud rate of the signal.
Some of the basic digital modulation techniques are –
Amplitude shift keying
Frequency shift keying
Phase shift keying

## Slide 15: Amplitude shift keying
In amplitude shift keying (ASK), when a bit stream is transmitted, a binary 1 is represented by the presence of the carrier signal c(t) for a specified interval of time, and a binary 0 is represented by the absence of the carrier signal for the same interval of time.
Mathematically, ASK can be represented as

## Slide 16: Amplitude shift keying
Where Ac is the amplitude of the carrier signal and fc is its frequency.
The result of ASK when applied to the bit pattern shown in Figure 1.4 (a) is shown in Figure 1.4 (b).

## Slide 17: Amplitude shift keying

## Slide 18: Frequency Shift Keying
Frequency shift keying (FSK) is done as follows.
If fc is the frequency of the carrier signal and if k is a small frequency offset, then transmission of a binary 1 is represented by the presence of a carrier signal of frequency fc + k for a specified interval of time.
Transmission of bit 0 is represented by the presence of a carrier signal of frequency fc − k for the same interval of time.

## Slide 19: Frequency Shift Keying
Two frequency levels are used in this technique, it is also known as two-level FSK or binary FSK (BFSK).
FSK can be mathematically represented as follows:
Where Ac and fc are the amplitude and frequency, respectively, of the cosine carrier signal.
FSK when applied to the bit pattern of Figure 1.5 (a) is shown in Figure 1.5 (b).

## Slide 20: Frequency Shift Keying

## Slide 21: Frequency Shift Keying
In the FSK mechanism described above, that is, BFSK, since only two frequency levels are used, each frequency level encodes just a single bit, 1 or 0.
By using multiple frequency levels (by using multiple frequency offsets), a single frequency level can be used to encode multiple bits.
An example is the four-level FSK.
A four-level FSK can be used to transmit two bits per frequency shift. It can be mathematically represented as-

## Slide 22: Frequency Shift Keying
Where Ac is the amplitude and fc is the frequency of the carrier signal.

## Slide 23: Phase Shift Keying
In phase shift keying (PSK), change in phase of the carrier signal is used to represent the 0 and 1 bits.
The transmission of bit 0 is represented by the presence of the carrier for a specific interval of time, while the transmission of bit 1 is represented by the presence of a carrier signal with a phase difference of π radians for the same interval of time.
PSK using a cosine carrier wave with amplitude Ac and frequency fc can be mathematically represented as-

## Slide 24: Phase Shift Keying
This technique is also known as binary PSK (BPSK) or two-level PSK since a single phase difference is used for representing 0 and 1 bits.
Figure 1.6 (b) shows the BPSK modulation of the bit pattern of Figure 1.4 (a).

## Slide 25: Phase Shift Keying

## Slide 26: Phase Shift Keying
Just as multiple frequency levels are used in FSK, multiple phase deviations can be used in PSK.
This enables encoding of multiple bits by each phase representation.
Quadrature PSK (QPSK), for example, uses four different phases each separated by π/2 radians.
This would enable transmission of two bits per phase shift.
The mathematical representation of QPSK is given below-

## Slide 27: Phase Shift Keying
π/4 shifted QPSK (π/4-QPSK) is a QPSK mechanism where the maximum phase deviation is limited to ± 135 degrees.
The main advantage of π/4 shifted QPSK is that it can be received non-coherently, that is, the receiver need not lock to the phase of the transmitted signal, which simplifies the receiver design.
It provides the bandwidth efficiency of QPSK along with lesser fluctuations in amplitude.