## Slide 1: MULTIPLE ACCESS TECHNIQUES

## Slide 2: MULTIPLE ACCESS TECHNIQUES
The transmission medium in wireless networks is broadcast in nature, a node (wireless communication device) cannot transmit on the channel whenever it wants to.
Multiple access techniques are used to control access to the shared channel.
They determine the manner in which the channel is to be shared by the nodes.

## Slide 3: MULTIPLE ACCESS TECHNIQUES
Multiple access techniques are based on the orthogonalization of signals, each signal represented as a function of time, frequency, and code.
Multiplexing can be performed with respect to one of these three parameters; the respective techniques are termed as frequency division multiple access, time division multiple access, and code division multiple access.
A part from these techniques, the medium can be multiplexed with respect to space also, and this technique is called space division multiple access.

## Slide 4: Frequency Division Multiple Access
In FDMA the available bandwidth is divided into multiple frequency channels/bands.
A transmitter–receiver pair uses a single dedicated frequency channel for communication.
The frequency spectrum is in effect divided into several frequency sub-bands.
Transmissions on the main band of a channel also result in the creation of additional signals on the side bands of the channel.
Hence the frequency bands cannot be close to each other.

## Slide 5: Frequency Division Multiple Access
Frequency bands are separated from each other by guard frequency bands in order to eliminate inter-channel interference.
These guard bands result in the underutilization of the frequency spectrum.
This is the main disadvantage of FDMA.
FDMA has been widely adopted in analog systems for portable telephones and automobile telephones.

## Slide 6: Frequency Division Multiple Access
Figure: Illustration of FDMA

## Slide 7: Frequency Division Multiple Access
In a cellular network, a central controller known as the base station (BS) dynamically allocates a different carrier frequency to each node, known as the mobile station (MS).
Each node is in fact allocated a pair of frequencies for communication, one for the traffic from the MS to the BS (uplink frequency), and the other for carrying traffic from the BS to the MS (downlink frequency).
This system, used for two-way communication between a pair of stations (MS and BS here), is called frequency division duplexing (FDD).
Since high-frequency transmissions suffer greater attenuation when compared to low-frequency transmissions, high transmission power is required for high-frequency channels for compensating the transmission losses.
Power available at an MS is limited. In order to conserve energy at the MS, the uplink frequency is always lower than the downlink frequency.

## Slide 8: Orthogonal Frequency Division Multiplexing
Orthogonal frequency division multiplexing (OFDM) is a multi-carrier transmission mechanism.
It resembles FDMA in that both OFDM and FDMA split the available bandwidth into a number of frequency channels.
OFDM is based on the spreading of the data to be transmitted over multiple carriers, each of them being modulated at a low rate.
The data signal is split into multiple smaller sub-signals that are then transmitted to the receiver simultaneously at different carrier frequencies (sub-carriers).
Splitting the carrier into multiple smaller sub-carriers and then broadcasting the sub-carriers simultaneously reduce the signal distortion at the receiver caused due to multipath propagation of the transmitted signal.
OFDM is sometimes also referred to as discrete multi-tone (DMT) modulation.
OFDM is currently used in several applications such as wireless local area networks (WLANs) and digital broadcasting.

## Slide 9: Time Division Multiple Access
Time division multiple access (TDMA) shares the available bandwidth in the time domain.
Each frequency band is divided into several time slots (channels).
A set of such periodically repeating time slots is known as the TDMA frame.
Each node is assigned one or more time slots in each frame, and the node transmits only in those slots.

## Slide 10: Time Division Multiple Access

## Slide 11: Time Division Multiple Access
For two-way communication, the uplink and downlink time slots, used for transmitting and receiving data, can be on the same frequency band (TDMA frame) or on different frequency bands.
TDMA is essentially a half-duplex mechanism, where only one of the two communicating nodes can transmit at a time, the small duration of time slots creates the illusion of a two-way simultaneous communication.

## Slide 12: Time Division Multiple Access
Perfect synchronization is required between the sender and the receiver.
To prevent synchronization errors and inter-symbol interference due to signal propagation time differences, guard intervals are introduced between time slots.
Since the sizes of slots are already small, the introduction of guard intervals results in a significant overhead for the system.

## Slide 13: Time Division Multiple Access
FDMA requires the device to have the capability of simultaneously receiving and transmitting signals, which leads to increased cost.
But when TDMA is used, the device can switch between slots and hence use the same transmitter for receiving also.
Hence, the equipment cost in TDMA is less.
TDMA is widely used in second generation cellular systems such as GSM.

## Slide 14: Code Division Multiple Access
Code division multiple access (CDMA) does not assign a specific frequency to each user as like FDMA & TDMA.
Instead, every channel uses the entire spectrum.
Individual conversations are encoded with a pseudorandom digital sequence.
As the narrow-band transmission frequency is spread over the entire wideband spectrum, the technique is also called as spread spectrum.

## Slide 15: Code Division Multiple Access
The transmissions are differentiated through a unique code that is independent of the data being transmitted, assigned to each user.
The orthogonality of the codes enables simultaneous data transmissions from multiple users using the entire frequency spectrum, thus overcoming the frequency reuse limitations seen in FDMA and TDMA.

## Slide 16: Code Division Multiple Access
CDMA was first used during World War II by the English Allies to foil attempts by the German army to jam the transmissions of the Allies.
The Allies decided to transmit signals over several frequencies in a specific pattern, instead of just one frequency, thereby making it very difficult for the Germans to get hold of the complete signal.
Two types of spread spectrum systems are widely in use today-
  Frequency hopping spread spectrum
  Direct sequence spread spectrum

## Slide 17: Frequency Hopping Spread Spectrum
FHSS is a simple technique in which the transmission switches across multiple narrow-band frequencies in a pseudo-random manner i.e, the sequence of transmission frequencies is known both at the transmitter and the receiver, but appears random to other nodes in the network.
The process of switching from one channel to the other is termed frequency hopping.

## Slide 18: Frequency Hopping Spread Spectrum
The radio frequency signal is de-hopped at the receiver by means of a frequency synthesizer controlled by a pseudo-random sequence generator.
The below figure shows two simultaneous transmissions.
The first transmission (darker shade in figure) uses the hopping sequence f4 f7 f2 f1 f5 f3 f6 f2 f3 and the second transmission uses the hopping sequence f1 f3 f6 f2 f4 f2 f7 f1 f5.
Frequency hopped systems are limited by the total number of frequencies available for hopping.

## Slide 19: Frequency Hopping Spread Spectrum
FHSS can be classified into two types: fast FHSS and slow FHSS.
In fast FHSS, the dwell time on each frequency is very small, i.e, the rate of change of frequencies is much higher than the information bit rate, resulting in each bit being transmitted across multiple frequency hops.
In slow FHSS, the dwell time on each frequency is high, hence multiple bits are transmitted on each frequency hop.
FHSS is now used mainly for short-range radio signals, particularly those in the unlicensed bands.

## Slide 20: Frequency Hopping Spread Spectrum

## Slide 21: Direct Sequence Spread Spectrum
Suppose conversations in several languages are occurring in a room.
People who understand only a particular language listen to and follow the conversation taking place in that language alone.
They ignore and discard conversations in other languages as noise.
The same principle applies to DSSS.

## Slide 22: Direct Sequence Spread Spectrum
In DSSS, each node is assigned a specific n-bit code, called a chipping code. n is known as the chipping rate of the system.
These codes assigned to the nodes are orthogonal to each other, i.e, the normalized inner product of the vector representations of any two codes is zero. Each node transmits using its code.
At the receiver, the transmission is received and information is extracted using the transmitter’s code.

## Slide 23: Direct Sequence Spread Spectrum
For transmitting a binary 1, the sender transmits its code; for a binary 0, the one’s complement of the code is transmitted.
Hence, transmission of a signal using CDMA occupies n times the bandwidth that would be required for a narrow-band transmission of the same signal.
Since the transmission is spread over a large bandwidth, resistance to multipath interference is provided for in CDMA.
DSSS is used in all CDMA cellular telephony systems.

## Slide 24: Direct Sequence Spread Spectrum

## Slide 25: Space Division Multiple Access
The fourth dimension in which multiplexing can be performed is space.
Instead of using omnidirectional transmissions (as in FDMA, TDMA, and CDMA) that cover the entire circular region around the transmitter, space division multiple access (SDMA) uses directional transmitters/antennas to cover angular regions.
Thus different areas/regions can be served using the same frequency channel.

## Slide 26: Space Division Multiple Access
This method is best suited to satellite systems, which often need a narrowly focused beam to prevent the signal from spreading too widely and in the process becoming too weak.
A satellite can thus reuse the same frequency to cover many different regions of the Earth’s surface.

## Slide 27: Space Division Multiple Access