## Slide 1: VOICE CODING

## Slide 2: VOICE CODING
The voice coding process converts the analog signal into its equivalent digital representation.
The analog speech information to be transmitted is first converted into a sequence of digital pulses.
It should then be transmitted without any noticeable distortion.
The devices that perform this analog to digital conversion (at the sender) and the reverse digital to analog signal conversion (at the receiver) are known as codecs (coder/decoder).

## Slide 3: VOICE CODING
The main goal of a codec is to convert the voice signal into a digital bit stream that has the lowest possible bit rate, while maintaining an acceptable level of quality of the signal.
It should be possible to reproduce the original analog speech signal at the receiver without any perceivable distortion or disturbances.

## Slide 4: Pulse Position Modulation
PPM is one of the techniques used for converting an analog signal into its digital representation.
In PPM, the amplitude and width of the pulse are kept constant.
The position of each pulse, with respect to the position of a recurrent reference pulse, is varied according to the instantaneous sampled amplitude of the information signal.

## Slide 5: Pulse Position Modulation
PPM requires constant transmitter power since all pulses have the same constant amplitude and duration.
PPM is used in the infrared physical layer specification of the IEEE 802.11 standard.
The main disadvantage of PPM is that perfect synchronization is required between the transmitter and receiver.

## Slide 6: Pulse Code Modulation
Pulse Code Modulation (PCM) is another technique which is commonly used for conversion of an analog signal into its corresponding digital form.
PCM essentially consists of three stages-
  Sampling of the analog signal
  Quantization
  Binary encoding

## Slide 7: Sampling
The codec converts the analog speech signal to its digital representation by sampling the signal at regular intervals of time.
The higher the sampling rate, that is, the shorter the time interval between successive samples, the better the description of the voice signal.
The frequency of the samples to be taken, such that quality of the voice signal is preserved, is given by the sampling theorem.

## Slide 8: Sampling
According to the sampling theorem, if the original voice signal has a limited bandwidth, that is, it does not contain any component with a frequency exceeding a given value B, then all information in the original signal will be present in the signal described by the samples, if the sampling frequency is greater than twice the highest frequency in the original signal, that is, it is greater than 2 × B.
This theorem is also known as Nyquist’s theorem.

## Slide 9: Sampling
The series of pulses produced after sampling the analog signal, known as pulse amplitude modulation (PAM) pulses, have their amplitudes proportional to that of the original signal.
Figure 1.1(b) shows the PAM pulses generated for the analog waveform of Figure 1.1 (a).

## Slide 11: Quantization
During the quantization phase, the amplitudes of the PAM pulses are measured and each pulse is assigned a numerical value.
In order to avoid having to deal with an infinite number of values for the PAM pulses, a fixed number of amplitude levels are used.
The amplitude of the analog signal at each sampling instant is rounded off to the nearest level.
Figure 1.1(c) depicts the output of quantization applied to the PAM pulses in Figure 1.1(b).

## Slide 12: Quantization
Since some of the information is lost due to the approximation of amplitude levels, quantization distorts the original analog signal.
This distortion is also known as quantization error.
But at the same time, since only a fixed number of amplitude levels are used, only a fixed number of numerical values need to be transmitted.
This reduces the complexity of the equipment and also the probability of transmission errors.

## Slide 14: Binary Encoding
In this final phase, the quantized PAM pulses are encoded into the binary format, which forms the final output of the analog-to-digital conversion process.
The number of bits used to represent each amplitude level is based on the total number of amplitude levels that need to be represented.
The quantized PAM pulses in Figure 1.1(c) use seven quantization levels.

## Slide 15: Binary Encoding
Therefore, at least three bits would be required for representing each level.
The encoded output of the quantized pulses in Figure 1.1(c) would be 110 110 100 010 011 110 110 101 100 100 101.
This bit pattern is then modulated and transmitted by the sender.

## Slide 16: Vocoders
The PCM mechanism described above requires high bit rates.
PCM is not very suitable for wireless networks where the limited bandwidth needs to be utilized efficiently.
Vocoders are devices that operate making use of knowledge of the actual structure and operation of human speech production organs.
They do not modulate the actual voice signal; instead they work by modeling the mechanics by which sound is produced (e.g., lip movement, and the effect of the throat and nose on speech).
This information is encoded and transmitted by the sender, and is received by the receiver, which then reconstructs the original signal.

## Slide 17: Vocoders
Vocoders achieve voice transfer at low bit rates.
Hence they are more suitable compared to PCM for voice communication in wireless networks.
But a drawback of using vocoders is that since the actual voice signals are not transmitted, the signals received and reconstructed at the receiver do not appear to be natural.
The artificiality in the reconstructed signal makes it difficult to identify the actual speaker on the other side.
In order to overcome the above problem, certain hybrid codecs are used, which transmit both vocoding information and also the PCM signal information.
Certain other codecs are also available, which vary the bit rate of the outgoing signal according to the characteristics of the speech signals fed to them.