## Slide 1: Computer Network Architecture

## Slide 2: Computer Network Architecture
The network layers, along with their respective protocols, constitute the computer network architecture.
Several such computer network architectures/ models are in existence today.
Prominent models such as
  OSI reference model
  TCP/IP reference model
  ATM reference model

## Slide 3: The OSI Reference Model
This model was proposed by the International Organization for Standardization (called ISO in short).
The objective of this standard was to standardize the protocols used in the various network layers.
This model was named as the open systems interconnection (OSI) reference model.
The main objective of the model was to specify mechanisms for communication between systems (machines) in a telecommunication network that are open for communication with other systems.

## Slide 4: The OSI Reference Model
The OSI reference model is depicted in below Figure.
It consists of seven layers, namely-
  Physical Layer
  Data Link Layer
  Network Layer
  Transport Layer
  Session Layer
  Presentation Layer
  Application Layer
Each layer is associated with a unique set of functions and responsibilities.

## Slide 5: The OSI Reference Model

## Slide 6: Physical Layer
The physical layer, which is the lowest layer, is responsible for the transmission of the bit stream over the physical medium.
It deals with the mechanical and electrical specifications of the network hardware and the physical transmission medium to be used for the transmissions.
The mechanical specifications refer to the physical dimensions of the devices such as cables, connectors, and pins used for interconnection.
The electrical specifications include details such as voltage levels to be used for representing digital information (binary 0s and 1s) and the duration of each bit.
The physical layer acts as a direct interface to the actual physical transmission medium.

## Slide 7: Data Link Layer
The main objective of the data link layer, is to ensure error-free transmission of data across a physical link.
It receives data from the higher layer, splits the data into several frames/packets, and transmits the frames.
It may have mechanisms for detecting and retransmitting damaged or lost frames.
The DLL is also responsible for implementing link-level congestion control mechanisms that ensure that a fast sender does not flood a slow receiver.
In broadcast networks, the DLL performs medium access control.
It determines when, i.e, at what point of time, the current node can access the channel for its transmissions so that collisions arising due to simultaneous transmissions by multiple nodes are minimized.

## Slide 8: Network Layer
The Network Layer is responsible for routing data packets from the source node to the destination node.
The network layer is also responsible for node addressing.
A packet may have to traverse across several networks in order to reach its destination.
Each of these networks might follow different addressing schemes.
The network layer has to make sure that this heterogeneity does not affect end-to-end packet delivery.
Congestion control in the local network is also the responsibility of the network layer.

## Slide 9: Transport Layer
The transport layer provides the higher layers a network independent interface to the lower layers.
The functions of the transport layer include segmentation and reassembly of messages, end-to-end error recovery, monitoring of quality of service (QoS), and end-to-end flow control.

## Slide 10: Session Layer
A session can be defined as a connection between two presentation layer (the next higher layer) processes.
It can be thought to be a connection between two users on two different machines.
The services provided by the session layer to the presentation layer are with respect to these sessions.
They include establishment and release of session connections, interaction management and synchronization between the two ends of the session.

## Slide 11: Presentation Layer
The presentation layer, the sixth layer from the bottom, is concerned with the syntax and semantics of the information exchanged between the two end systems.
The presentation layer ensures that the messages exchanged between two processes that reside on the different computers that use different data representations, have a common meaning.
In order for such computers to communicate, the data structures that need to be transmitted can be defined in a common abstract manner.
Other functions of the presentation layer include data encryption and data compression.

## Slide 12: Application Layer
The top-most layer in the OSI protocol stack is the application layer.
The application layer acts as an interface to the application processes that require communication support.
It provides mechanisms for supporting tasks such as data transmission between users, distributed database access, running processes on remote machines, controlling distributed systems, and electronic mail communication.

## Slide 13: Application Layer
Some examples of protocols used in this layer are-
  Virtual Terminal (TELNET), which provides remote login facility for users.
  File Transfer Protocol (FTP), used for transferring files between machines.
  Simple Mail Transfer Protocol (SMTP), is used for electronic mail applications.
  Hyper Text Transfer Protocol (HTTP), which is used for transferring Web pages over the Internet.

## Slide 14: The TCP/IP Reference Model
The TCP/IP reference model is the network model that is used in today’s Internet.
The model is widely referred to as TCP/IP protocol stack since it was originally designed as a protocol stack for the Advanced Research Project Agency Network (ARPANET) rather than as a reference model.
It is named so after two of its main protocols, transmission control protocol (TCP) and Internet protocol (IP).

## Slide 15: The TCP/IP Reference Model
In contrast to the OSI reference model, the TCP/IP reference model has only four layers.
This model was far better than the OSI model because the protocols that are part of this model were already in use before the model was actually designed.
The four layers of the TCP/IP model are-
  The host-to-network layer
  Internet/network layer
  Transport layer
  Application layer
The session and presentation layers that found place in the OSI reference model were not included in the TCP/IP model since they were found to be not very significant.

## Slide 16: The TCP/IP Reference Model

## Slide 17: Host-to-Network Layer
The lowest layer, the host-to-network layer, is used to interface the TCP/IP protocol stack with the physical transmission medium.
The operation of this layer is not very well-specified in the TCP/IP model.
The host machine should connect to the network using some protocol in order to transmit the packets sent to it by the next higher layer, the internet layer.

## Slide 18: Internet Layer
This layer is similar in functionality to the network layer in the OSI reference model.
The main functions of the internet layer are routing and congestion control.
The internet layer should provide mechanisms for the host to inject packets into any network and have those packets travel independently to the destination.
The internet layer defines a protocol called Internet protocol (IP).
The packets sent by the internet layer to the lower layer follow this IP format.
The routing of packets is done on an individual packet-by-packet basis.
Hence the packets may arrive out of order at the destination. It is the responsibility of the next higher layer, the transport layer, to reorder the received packets.

## Slide 19: Transport Layer
The transport layer in the TCP/IP model performs similar operations as the transport layer in the OSI reference model.
The design of the transport layer in the OSI model was actually influenced by the operation and performance of TCP.
Two end-to-end communication protocols, the transmission control protocol (TCP) and the user datagram protocol (UDP), have been defined in this layer.

## Slide 20: TCP
TCP is a reliable connection-oriented protocol.
Here, establishment of an end-to-end connection that may traverse multiple hops is required before the actual data transfer can begin.
All packets belonging to a session follow the same path, and are received at the destination in the same order as they were transmitted by the source node.
The incoming byte stream at the source node is split into several messages and sent to the internet layer.
The received messages are reassembled by the transport layer at the destination.
In order that a fast sender does not swamp a slow receiver, TCP also performs flow control.

## Slide 21: UDP
UDP is an unreliable connectionless protocol.
It does not have the flow control and sequencing mechanisms present in TCP.
UDP is used by applications such as voice/video transmissions where fast delivery of information is more important than the accuracy of the information delivered.

## Slide 22: Application Layer
The application layer is the topmost layer in the TCP/IP model.
It consists of higher-level protocols, which include the FTP, TELNET, SMTP, and HTTP.

## Slide 23: The ATM Reference Model
The asynchronous transfer mode (ATM) model was developed by the ITU for broadband-integrated services digital network (B-ISDN).
The ATM model is quite different from the OSI and TCP/IP reference models.
Here, all information is transmitted in the form of short fixed-sized packets called cells.
The size of each cell is 53 bytes, a 5-byte header followed by a 48- byte payload.

## Slide 24: The ATM Reference Model
The asynchronous transfer mode (ATM) model was developed by the ITU for broadband-integrated services digital network (B-ISDN).
The ATM model is quite different from the OSI and TCP/IP reference models.
Here, all information is transmitted in the form of short fixed-sized packets called cells.
The size of each cell is 53 bytes, a 5-byte header followed by a 48- byte payload.
ATM uses a switching technology called cell switching.
The two other commonly used switching technologies are -
  Packet Switching
  Circuit Switching

## Slide 25: Circuit switching
Circuit switching requires the setting up of an end-to-end path between the source and destination nodes before the actual data transmission begins.
A request packet sent by the source node travels till the destination node.
The destination responds with an acknowledgment.
When the source node receives this acknowledgment, implying that the path has been set up, it starts transmitting packets.
The request-response process also reserves the required resources (bandwidth) on the path.
Once a path is set up, all packets belonging to the flow follow the same path.
The packets are received at the destination in the same order they were transmitted at the source.

## Slide 26: Circuit switching
Circuit switching is widely used in telephone networks where once a connection is established between the two end users, the circuit (connection) continuously remains open from the start till completion of the call.
Circuit switching may not be suitable for data or other non-conversational transmissions.
Non-voice transmissions tend to occur in bursts, and if circuit switching is used for such transmissions, the transmission line often remains idle, resulting in under-utilization of the available network capacity.

## Slide 27: Message Switching
Here the sender transmits data in blocks.
There is no limit on the size of the blocks.
An intermediate node receives the entire block of data from its uplink node, stores the block in its disk, checks for errors, and then transmits it to the next downlink node.
Since there is no limit on the size of blocks transmitted, a single large block of data may hog the channel for a long period of time.
Hence, message switching is not suitable for interactive applications and time-sensitive applications such as voice and video transmissions.
The third and most widely used switching technique, packet switching, solves the above problems.

## Slide 28: Packet Switching
In packet switching, a strict bound is set on the maximum size of the blocks transmitted.
The packets will be held in the main memory of intermediate routers rather than in their disks.
A node can transmit each packet independently.
Unlike message switching, it need not wait for a whole block of data (consisting of many packets) to be received before the transmission of the received block can be started.
Hence, the end-to-end delay involved is less, and the throughput of the system is also high.
Since resources are not reserved beforehand, the links may become congested when the network load increases, resulting in packet loss.
In packet switching, each packet is routed (and not switched) independently at each intermediate node.
Packets belonging to the same flow may hence take different paths to reach the destination.
Due to this, it is highly probable that the packets are received out of order at the destination node.

## Slide 29: cell switching
Cell Switching is similar to packet switching in that it splits a data stream into multiple equal-sized cells which are then transmitted on a channel that is shared by other nodes also.
The main difference between cell and packet switching techniques is that while cells have a fixed size, packets can have different sizes.
One of the main reasons for having fixed-length cells is to facilitate the building of fast hardware switches.
The design of fast and highly scalable hardware switches would be made simple if all packets were of fixed length.
The processing of packets would be made simple if the size of the packets were known beforehand.
Also, parallelism could be incorporated into the switching system if all packets were of the same length; multiple switching elements could be working in parallel performing the same operation on different packets.
This improves the scalability of the switching system. Hence, the ATM design had fixed length cells.

## Slide 30: The ATM Reference Model
Unlike the previous two models, the ATM model has been defined as a three-dimensional model consisting of layers and planes.
The three main layers are-
  Physical Layer
  ATM Layer
  ATM Adaptation Layer
The three planes used in this model are-
  User Plane
  Control Plane
  Management Plane

## Slide 32: The ATM Reference Model
The user plane is responsible for operations such as cell transport, error control, and flow control.
The control plane deals with connection management.
Operations on this plane are call setup and call tear-down.
The management plane maintains the network and carries out operational functions.
This plane is subdivided into layer management and plane management to manage the different layers and planes.
The concept of user and control planes enables streamlining of the implementation in each plane, which improves the performance of the system.

## Slide 33: Physical Layer
This layer is divided into two sublayers.
The lower sublayer, called the physical medium dependent (PMD) sublayer, directly interfaces with the physical medium and takes care of the actual transmission of bits and the bit timing.
The upper sublayer of the physical layer is called the transmission convergence (TC) sublayer.
At the sender side, the TC sends the incoming cells as a string of bits to the PMD, which transmits the bit stream.
At the receiver, the TC sublayer receives the bit stream from the PMD sublayer.
The TC sublayer, which is aware of details such as where cells begin and end (cell boundaries), then converts the incoming bit stream into cells and delivers them to the next higher layer, the ATM layer.

## Slide 34: ATM layer
The ATM layer is the core and the most important layer of the ATM reference model.
It is responsible for routing cells across the network.
Functions of the ATM layer include definition of the cell layout, establishment and release of virtual circuits, and congestion control.
The ATM layer is equivalent to the combined network and data link layers in the OSI reference model.

## Slide 35: ATM Adaptation Layer (AAL)
This layer is where user information is created and received as 48-byte payloads.
It consists of two sublayers, a segmentation and reassembly (SAR) sublayer and a convergence sublayer (CS).

## Slide 36: Convergence Sublayer
The CS sublayer which is the upper sublayer packages the higher layer’s PDUs(protocol data unit) with any additional information required for adapting them to the ATM service.
On receiving a higher-layer PDU, the CS sublayer adds a header and trailer to the received PDU, resulting in a CS-PDU, which is passed on to the lower SAR sublayer.

## Slide 37: Segmentation and Reassembly (SAR)
On the sender side the SAR sublayer segments/breaks the PDUs received from the higher layers into cells, and at the receiver side it reassembles/puts them back together again.

## Slide 38: Segmentation and Reassembly (SAR)
When a CS-PDU is received by the SAR sublayer at the sender, it breaks it into small units, adds its own header and trailer to each unit, and the resultant 48-byte unit is known as SAR-PDU.
This SAR-PDU is sent to the ATM layer, which adds a 5-byte header, resulting in a 53- byte ATM-PDU or what is known as a cell.
The reverse process takes place at the receiver.
The SAR sublayer collects multiple SAR-PDUs, strips off the headers and trailers, assembles a CS-PDU, and sends it to the CS sublayer.
The CS sublayer in turn removes its own header and trailer and gives the resulting higher-layer PDU to the higher layer.