## Slide 1: IEEE 802 Networking Standards

## Slide 2: IEEE 802 NETWORKING STANDARD
The Institute of Electrical and Electronics Engineers (IEEE) has defined several standards for LANs.
IEEE 802 standards contains various protocols for data sharing.
IEEE 802 standards has following features such as-
  802.1 – internetworking
  802.2 - logical link control
  802.3 - Ethernet or CSMA/CD
  802.4 - token bus LANs
  802.5 - token ring LANs
  802.6 - MANs
  802.7 - broadband LANs

## Slide 3: IEEE 802 NETWORKING STANDARD
  802.8 - fiber optic LANs and MANs
  802.9 - integrated (voice/data) services LANs and MANs
  802.10 - security in LANs and MANs
  802.11 - wireless LANs
  802.12 – demand priority access LANs
  802.15 - wireless PANs
  802.16 - broadband wireless MANs
The IEEE 802 standard deals with the data link layer and the physical layer of the OSI reference model.
It defines rules for cabling, signaling, and media access control, which assure interoperability between network products manufactured by different vendors.

## Slide 4: IEEE 802.3 Standard
IEEE 802.3 is a standard for CSMA/CD networks & It is commonly referred as Ethernet standard.
IEEE 802.3 defines the physical layer and the MAC sublayer for CSMA/CD LANs.
The traditional Ethernet specification supports data transmission speeds of 10 Mbps.
Additional specifications such as fast Ethernet (IEEE 802.3u) and gigabit Ethernet (IEEE 802.3z) have been published to extend the performance of traditional Ethernet up to 100 Mbps and 1,000 Mbps speeds.

## Slide 5: Physical Layer
Four types of cabling have been specified in the 802.3 standard.
They use the following physical transmission media:
  thick coaxial
  thin coaxial
  twisted pair
  optic fiber

## Slide 6: Thin coaxial
The first type of cabling called 10Base2 or thin Ethernet uses thin coaxial cable.
Until recently, this was the most popular 802.3 cable because it was cheap and since standard BNC (British Naval Connector) connectors, rather than vampire taps, were used to form T-junctions, the quality of the connection between the computer and the coaxial cable was good.
It operates at 10 Mbps, uses baseband signaling, and can support LAN segments (a LAN segment is a single section of network media that connects computers/nodes) of lengths up to 200 m.
Each segment can have up to 30 nodes.

## Slide 7: Thick coaxial
The second type of cabling, which uses thick coaxial cable, is called 10Base5 cabling. It is commonly referred to as thick Ethernet.
Connections are made using vampire taps, i.e, the connection is made by forcing a pin halfway into the coaxial cable’s core.
This results in a poor connection between the computer and the coaxial cable.
This system is called 10Base5 as it operates at 10 Mbps, uses baseband signaling (i.e., the signal is transmitted at its original frequency without using any modulation), and supports LAN segments of lengths up to 500 meters.
It can support up to 100 nodes per segment.

## Slide 8: Twisted pair
In the above two cabling techniques, detecting cable breaks, bad taps, or loose connections could be very tedious.
These problems with coaxial cabling systems made people switch to the 10Base-T cabling system.
In the 10Base-T system each node has a separate cable connecting it to a central hub.
Unshielded twisted pair (UTP) is the most commonly used cable for this system.
10Base-T supports a maximum segment length of 100 m with a maximum of 1,024 nodes per segment.

## Slide 9: Optic Fiber
The fourth cabling technique, called 10Base-F, uses fiber optic cable.
10Base-F is costlier compared to the other three schemes.
It offers excellent noise immunity.
It is the preferred cabling system when the distance between two connecting points is large.
It can support segments of lengths up to 2000 m, with a maximum of 1,024 nodes per segment.

## Slide 10: Table 1.3. Physical layer cabling

## Slide 11: MAC Sublayer
The MAC sublayer uses CSMA/CD technology.
When a node wants to transmit a frame, it listens to the channel (cable) to check whether there are any on-going transmissions.
If the channel is busy, the node waits for a random duration of time and attempts again. If the channel is idle, the node starts transmitting.
In order to minimize the duration of collisions in such circumstances, a transmitting node listens to what it is sending.
If what it hears is different from what it is sending, then it implies that a collision has occurred.
On detecting a collision, a transmitting node stops its data transmission and transmits a brief jamming signal.
The jamming signal ensures that all other nodes get to know that there has been a collision.
Any other simultaneously transmitting node, on hearing this jamming signal, stops its transmission.
After transmitting the jamming signal, the node waits for a random period of time, and then attempts to transmit again.
A receiver node operates as below-
  It listens to all frames on the cable.
  If the address of the frame is the same as that of its own address, or is the same as that of the group address of nodes of which the current node is a member, it copies the frame from the cable.
  Otherwise it just ignores the frame.

## Slide 12: MAC Sublayer

## Slide 13: MAC Sublayer
The frame starts with a 7-byte preamble & used for synchronization purposes.
Each byte in the preamble contains the bit pattern 10101010.
The Start-of-frame delimiter is a single byte, 10101011, which is a frame flag, indicating the start of a frame.
The start-of-frame field is followed by the destination address and source address fields.
Each manufacturer of Ethernet network cards assigns a unique 48-bit Ethernet address to every Ethernet card manufactured.
If all the bits are 1 in the destination address, the message is received by all computers connected to the cable, that is, broadcast.
If the first bit is 1, then the rest of the bits indicate a multicast group address; the frame would be delivered only to those nodes that are part of that particular multicast group.
If the first bit is 0, the rest of the bits make up a normal node address, which is unique to that node on that LAN.

## Slide 14: MAC Sublayer
The length field denotes the number of bytes present in the data field.
It can vary from a minimum of 0 to a maximum of 1,500 bytes.
If the frame length is less than 64 bytes, the Pad field is used to fill up the frame to 64 bytes.
The Checksum field is used to detect if any data bits have been corrupted during transmission.

## Slide 15: IEEE 802.11 Standard
The IEEE 802.11 standard is one of the most popular standards for wireless LANs.
Wireless LANs are used for providing network services in places where it may be very difficult or too expensive to lay cabling for a wireline network.
The IEEE 802.11 standard comes under the IEEE 802.x LAN standards, and specifies the physical layer and the MAC layer, adapted to the specific requirements of wireless LANs.
The objective of this standard is to provide wireless connectivity to wireless devices/nodes that require rapid deployment, which may be portable, or which may be mounted on moving vehicles within a local area.

## Slide 16: IEEE 802.11 Standard
The IEEE 802.11 standard also aids the regulatory bodies in standardizing access to one or more radio frequency bands for the purpose of local area communication.
The interfaces offered by 802.11 to the higher layers are the same as those offered in other 802.x standards.
The MAC layer should be able to work with multiple physical layers catering to multiple transmission techniques such as infrared and spread spectrum

## Slide 17: Physical Layer
The basic 802.11 standard supports three different physical layers.
Two of them, frequency hopping spread spectrum (FHSS) and direct sequence spread spectrum (DSSS) are based on radio transmissions, and the third is based on infrared.
The physical layer provides mechanisms for sensing the wireless channel and determining whether or not it is idle.
This mechanism is also called clear channel assessment (CCA).

## Slide 18: MAC Sublayer
The 802.11 standard follows carrier sense multiple access with collision avoidance (CSMA/CA), which is a random access scheme with carrier sensing and collision avoidance through random back-off.
Because of the nature of the radio environment, it is very difficult for a transmitting node to detect packet collisions in the network.
Hence, CSMA/CD is not preferred in wireless LANs.

## Slide 19: 802.11 Task Groups
Several task groups have been working on different networking aspects of wireless LANs.
The various 802.11 task groups are listed below.
  802.11
  802.11a
  802.11b
  802.11c
  802.11d
  802.11e
  802.11f
  802.11g
  802.11h
  802.11i
  802.11j
  802.11n

## Slide 20: 802.11
This was the first 802.11 task group.
The objective of this group was to develop MAC layer and physical layer specifications for wireless connectivity for fixed, portable, and mobile nodes within a local area.
The 802.11 standard was first published in 1997.

## Slide 21: 802.11a
This group created a standard for wireless LAN operations in the 5 GHz frequency band, where data rates of up to 54 Mbps are possible.
The 802.11a standard was ratified in 1999.

## Slide 22: 802.11b
This task group created a standard for wireless LAN operations in the 2.4 GHz Industrial, Scientific, and Medical (ISM) band, which is freely available for use throughout the world.
This standard is popularly referred to as Wi-Fi, standing for Wireless-Fidelity.
It can offer data rates of up to 11 Mbps.
This standard was ratified in 1999.

## Slide 23: 802.11c
This group was constituted for devising standards for bridging operations.
Manufacturers use this standard while developing bridges and access points.
The standard was published in 1998.

## Slide 24: 802.11d
This group’s main objective is publishing definitions and requirements for enabling the operation of the 802.11 standard in countries that are not currently served by the standard.
This standard was published in 2001.

## Slide 25: 802.11e
The main objective of this group is to define an extension of the 802.11 standard for quality of service (QoS) provisioning and service differentiation in wireless LANs.
Work is in progress in this regard.

## Slide 26: 802.11f
This group was created for developing specifications for implementing access points and distribution systems following the 802.11 standard, so that interoperability problems between devices manufactured by different vendors do not arise.
This standard was published in 2003.

## Slide 27: 802.11g
This group was involved in extending the 802.11b standard to support high-speed transmissions of up to 54 Mbps in the 5 GHz frequency band, while maintaining backward compatibility with current 802.11b devices.
The 802.11g standard was published in 2003.

## Slide 28: 802.11h
This is supplementary to the 802.11 standard.
It was developed in order for the MAC layer to comply with European regulations for 5 GHz wireless LANs, which require products to have mechanisms for transmission power control and dynamic frequency selection.
The standard was published in 2003.

## Slide 29: 802.11i
This group is working on mechanisms for enhancing security in the 802.11 standard.

## Slide 30: 802.11j
This task group is working on mechanisms for enhancing the current 802.11 MAC physical layer protocols to additionally operate in the newly available Japanese 4.9 GHz and 5 GHz bands.

## Slide 31: 802.11n
The objective of this group is to define standardized modifications to the 802.11 MAC and physical layers such that modes of operation that are capable of much higher throughputs at the MAC layer, with a maximum of at least 100 Mbps, can be enabled.
Work on this is in progress.