## Slide 1: Wireless Network

## Slide 2: Wireless Network
Wireless networks are computer networks that use radio frequency channels as their physical medium for communication.
Each node in the network broadcasts information which can be received by all nodes within its direct transmission range.
Since nodes transmit and receive over the air, they need not be physically connected to any network.
These networks offer data connectivity along with user mobility.

## Slide 3: Wireless Network
The world’s first wireless radio communication system was invented by Guglielmo Marconi in 1897.
In 1901, he successfully demonstrated his wireless telegraph system to the world by transmitting radio signals across the Atlantic Ocean from England to America, covering more than 1,700 miles.
Through his system, two end users could communicate by sending each other alphanumeric characters that were encoded in an analog signal.
This signaled the beginning of the radio communications era.

## Slide 4: Wireless Network
Today, very advanced communication systems are available.
Radio and television broadcasting are some of the very common applications that cannot do without wireless technologies.
Voice communication has been the biggest beneficiary of the developments that took place, and are still taking place, in wireless communication technologies.
Beginning in the 1960s, several communication satellites have been launched, and today a huge proportion of long-distance voice communication takes place through the numerous satellites orbiting around the Earth.

## Slide 5: Wireless Network
Wireless communications is one of the fastest growing industries in the world.
The wireless communications industry has several segments such as cellular telephony, wireless LANs, and satellite-based communication networks.
The major portion of the growth in wireless industry has been due to cellular networks.
The early 1980s saw the commercial deployments of the world’s first mobile cellular networks.

## Slide 6: Wireless Network
Cellular networks provide two-way simultaneous voice communication.
A fixed base station serves all mobile phones in its coverage area, also called a cell.
The entire service area is divided into a number of non-overlapping cells (in actual deployments the cells overlap partially), communication within each cell being coordinated by a separate base station.

## Slide 7: First Generation
The first-generation (1G) cellular networks used analog signal technology.
They used frequency modulation for signal transmission.
The mobile phones were bulky and not very compact.
The coverage provided by the 1G networks was also not good.
The 1G system deployed in the United States and Canada was known as the advanced mobile phone system (AMPS).

## Slide 8: Second Generation
Second-generation (2G) cellular systems used digital transmission mechanisms such as TDMA and CDMA.
The global system for mobile communication (GSM) used in Europe, the IS-136 (Telecommunications Industry Association Interim Standard) system used in the United States, and the personal digital communication (PDC) system used in Japan are some of the popular 2G cellular systems.
The 1G and 2G systems were designed primarily for voice communication.

## Slide 9: GPRS(2.5G)
The present generation of wireless communication networks is often called 2.5G.
2.5G is usually associated with the general packet radio services (GPRS) system.
GPRS has been commercially deployed in many countries.

## Slide 10: Third Generation
The third-generation (3G) systems are expected to provide services such as enhanced multimedia, bandwidth up to 2 Mbps, and roaming capability throughout the world.
Commercial large scale deployments of 3G systems have not yet started.
It is estimated that communication service providers would shift to 3G by 2005.
Wideband code division multiple access (W-CDMA) and universal mobile telecommunications system (UMTS) are some of the important 3G standards.

## Slide 11: Fourth Generation
Standardization efforts are on for the fourth-generation (4G) wireless networks.
The 4G systems are expected to provide further improvements in the services provided by 3G, such as enhanced multimedia, universal access, and portability across all types of devices.
4G services are expected to be commercially introduced by 2010.
The deployment of 4G services would transform the world truly into a global village.
LTE (Long Term Evolution)

## Slide 12
Though the 2G and 2.5G systems were well-suited for voice communication, what fueled the development of newer technologies such as 3G and 4G, was the realization that wireless data services would also become very important in the next few years.
Wireless data services are projected to be another huge market for the telecommunications companies.
Wireless Internet forms the core of these data services.
Wireless access to the Internet using mobile phones would require several modifications to the already existing Internet protocols, since such devices have limited display and input capabilities.
Work is in progress for developing such protocols.

## Slide 13: Wireless local area networks
Wireless local area networks (WLANs) are another type of wireless networks that are increasingly popular today.
WLANs are used for providing network services in places where it is very difficult or is too expensive to lay cabling for a wireline network.
In a WLAN, a stationary node called an access point (AP) coordinates the communication taking place between nodes in the LAN.
The two main standards for WLANs are the IEEE 802.11 standard and the European Telecommunications Standards Institute (ETSI) HIPERLAN standard.

## Slide 14: Wireless personal area networks (WPANs)
Wireless personal area networks (WPANs) are short-distance wireless networks that have been specifically designed for interconnecting portable and mobile computing devices such as laptops, mobile phones, pagers, personal digital assistants (PDAs), and a number of other consumer electronic devices.
Bluetooth is a popular WPAN specification and it defines how data is managed and physically carried over the WPAN.
The typical range of a Bluetooth network is around 10 m.
The Bluetooth Special Interest Group (SIG), comprised of several leading companies such as Ericsson, Intel, IBM, Nokia, and Toshiba, is driving the development of the Bluetooth technology and bringing it to the market.
The IEEE 802.15 standard defines specifications for the media access control and physical layers for wireless devices in WPANs.

## Slide 15: Ad hoc wireless network.
Another emerging type of wireless network is the ad hoc wireless network.
An ad hoc wireless network is an autonomous system of mobile nodes connected through wireless links.
It does not have any fixed infrastructure (such as base stations in cellular networks).
The mobile stations/nodes in the network coordinate among themselves for communication.
Hence, each node in the network, apart from being a source or destination, is also expected to route packets for other nodes in the network.
Such networks find varied applications in real-life environments such as communication in battlefields, communication among rescue personnel in disaster affected areas, law enforcement agencies, and wireless sensor networks.

## Slide 16: Other Wireless Networks
The networks mentioned so far are either infrastructure-based where fixed base stations/access points are used, or infrastructure-less where no fixed infrastructure support is available.
Several new hybrid networking architectures are emerging that are a combination of the above two types of networks, taking advantage of the best features of both.
Some examples of such hybrid wireless network architectures are multi-hop cellular network (MCN), integrated cellular and ad hoc relaying system (iCAR), and multi-power architecture for cellular networks (MuPAC).