## Slide 1: UNIT-IV
Quality Of Service In Ad Hoc Wireless Networks

## Slide 2: SYLLABUS
Introduction
Issues and Challenges in Providing QOS in Ad Hoc Wireless Networks
Classifications of QoS Solutions
MAC Layer Solutions
Network Layer Solutions
QoS Frameworks for Ad Hoc Wireless Networks

## Slide 3: Introduction
Real-Time Traffic Support in Ad Hoc Wireless Networks
QoS Parameters in Ad Hoc Wireless Networks

## Slide 4: Introduction
QoS – A set of service requirements that are met by the network while transferring a packet stream from a source to a destination.
It is the performance level of a service offered by the network to the user.
The goal of QoS provisioning is to achieve a more deterministic network behavior, so that information carried by the network can be better delivered and network resources can be better utilized.

## Slide 5: Introduction
A network or a service provider can offer different kinds of services to the users.
A service can be characterized by a set of measurable prespecified service requirements such as minimum bandwidth, maximum delay, and maximum packet loss rate.
After accepting a service request from the user, the network has to ensure that the service requirements of the user’s flow are met, as per the agreement, throughout the duration of the flow.

## Slide 6: Introduction
After receiving a service request from the user, the first task is to find a suitable loop-free path from the source to the destination that will have the necessary resources available to meet the QoS requirements of the desired service.
This process is known as QoS routing.
After finding a suitable path, a resource reservation protocol is employed to reserve necessary resources along that path.
QoS guarantees can be provided only with appropriate resource reservation techniques.

## Slide 7: Introduction
Consider the network shown in below figure.
The attributes of each link are shown in a tuple <BW,D>, where BW and D represent available bandwidth in Mbps and delay in milliseconds.
Suppose a packet-flow from node B to node G requires a bandwidth guarantee of 4 Mbps.
QoS routing searches for a path that has sufficient bandwidth to meet the bandwidth requirement of the flow.
Here, six paths are available between nodes B and G as shown in below table.

## Slide 8: An example of QoS routing in ad hoc wireless network

## Slide 9: Available paths from node B to node G
QoS routing selects path 3 (i.e., B → C → F → G) because, out of the available paths, path 3 alone meets the bandwidth constraint of 4 Mbps for the flow.

## Slide 10: Introduction
The end-to-end bandwidth of a path is equal to the bandwidth of the bottleneck link (i.e., the link having minimum bandwidth among all the links of a path).
The end-to-end delay of a path is equal to the sum of delays of all the links of a path.
Clearly, path 3 is not optimal in terms of hop count and/or end-to-end delay parameters, while path 1 is optimal in terms of both hop count and end-to-end delay parameters.
Hence, QoS routing has to select a suitable path that meets the QoS constraints specified in the service request made by the user.

## Slide 11: Introduction
QoS provisioning often requires negotiation between host and network, call admission control, resource reservation, and priority scheduling of packets.
QoS can be rendered in ad hoc wireless networks through several ways, namely, per flow, per link, or per node.
In ad hoc wireless networks, the boundary between the service provider (network) and the user (host) is not defined clearly, thus making it essential to have better coordination among the hosts to achieve QoS.
Characteristics of ad hoc wireless networks such as lack of central coordination, mobility of hosts, and limited availability of resources make QoS provisioning very challenging.

## Slide 12: Real-Time Traffic Support in Ad Hoc Wireless Networks
Real-time applications require mechanisms that guarantee bounded delay and delay jitter.
The end-to-end delay in packet delivery includes-
  queuing delay at the source and intermediate nodes
  processing time at the intermediate nodes
  propagation duration over multiple hops from the source node to the destination node.
Real-time applications can be classified as hard real-time applications and soft real-time applications.

## Slide 13: Hard real-time application
A hard real-time application requires strict QoS guarantees.
Some of the hard real-time applications include nuclear reactor control systems, air traffic control systems, and missile control systems.
In these applications, failure to meet the required delay constraints may lead to disastrous results.
Providing hard real-time guarantees in ad hoc wireless networks is extremely difficult due to reasons such as the unrestricted mobility of nodes, dynamically varying network topology, time-varying channel capacity, and the presence of hidden terminals.

## Slide 14: Soft real-time applications
Soft real-time applications can tolerate degradation in the guaranteed QoS to a certain extent.
Some of the soft real-time applications are voice telephony, video-on-demand, and video conferencing.
In these applications, the loss of data and variation in delay and delay jitter may degrade the service but do not produce hazardous results.
Research community is currently focusing on providing QoS support for applications that require soft real-time guarantees.

## Slide 15: QoS Parameters in Ad Hoc Wireless Networks
As different applications have different requirements, the services required by them and the associated QoS parameters differ from application to application.
For example, In multimedia applications, bandwidth, delay jitter, and delay are the key QoS parameters.
In military applications have stringent security requirements.
For applications such as emergency search-and-rescue operations availability of the network is the key QoS parameter.
Applications such as group communication in a conference hall require that the transmissions among nodes consume as little energy as possible (battery life is the key QoS parameter here).

## Slide 16: QoS Parameters in Ad Hoc Wireless Networks
Unlike traditional wired networks, where the QoS parameters are mainly characterized by the requirements of multimedia traffic, in ad hoc wireless networks the QoS requirements are more influenced by the resource constraints of the nodes.
Some of the resource constraints are battery charge, processing power, and buffer space.