## Slide 1: Issues and Challenges in Providing QOS in Ad Hoc Wireless Networks

## Slide 2: ISSUES AND CHALLENGES IN PROVIDING QOS IN AD HOC WIRELESS NETWORKS
Providing QoS support in ad hoc wireless networks is an active research area.
Ad hoc wireless networks have certain unique characteristics that pose several difficulties in provisioning QoS.
Some of the characteristics are-
  Dynamically varying network topology
  Lack of precise state information
  Lack of a central controller
  Error-prone shared radio channel
  Hidden terminal problem
  Limited resource availability
  Insecure medium

## Slide 3: Dynamically varying network topology
Since the nodes in an ad hoc wireless network do not have any restriction on mobility, the network topology changes dynamically.
Hence, the admitted QoS sessions may suffer due to frequent path breaks, thereby requiring such sessions to be reestablished over new paths.
The delay incurred in reestablishing a QoS session may cause some of the packets belonging to that session to miss their delay targets/deadlines, which is not acceptable for applications that have stringent QoS requirements.

## Slide 4: Imprecise state information
In most cases, the nodes in an ad hoc wireless network maintain both the link-specific state information and flow-specific state information.
The link-specific state information includes bandwidth, delay, delay jitter, loss rate, error rate, stability, cost, and distance values for each link.
The flow-specific information includes session ID, source address, destination address, and QoS requirements of the flow (such as maximum bandwidth requirement, minimum bandwidth requirement, maximum delay, and maximum delay jitter).
The state information is inherently imprecise due to dynamic changes in network topology and channel characteristics.
Hence, routing decisions may not be accurate, resulting in some of the real-time packets missing their deadlines.

## Slide 5: Lack of central coordination
Unlike wireless LANs and cellular networks, ad hoc wireless networks do not have central controllers to coordinate the activity of nodes.
This further complicates QoS provisioning in ad hoc wireless networks.

## Slide 6: Error-prone shared radio channel
The radio channel is a broadcast medium by nature.
During propagation through the wireless medium, the radio waves suffer from several impairments such as attenuation, multipath propagation, and interference.

## Slide 7: Hidden terminal problem
The hidden terminal problem is inherent in ad hoc wireless networks.
This problem occurs when packets originating from two or more sender nodes, which are not within the direct transmission range of each other, collide at a common receiver node.
It necessitates the retransmission of the packets, which may not be acceptable for flows that have stringent QoS requirements.

## Slide 8: Limited resource availability
Resources such as bandwidth, battery life, storage space, and processing capability are limited in ad hoc wireless networks.
Out of these, bandwidth and battery life are critical resources, the availability of which significantly affects the performance of the QoS provisioning mechanism.
Hence, efficient resource management mechanisms are required for optimal utilization of these scarce resources.

## Slide 9: Insecure medium
Due to the broadcast nature of the wireless medium, communication through a wireless channel is highly insecure.
Therefore, security is an important issue in ad hoc wireless networks, especially for military and tactical applications.
Ad hoc wireless networks are susceptible to attacks such as eavesdropping, spoofing, denial of service, message distortion, and impersonation.
Without sophisticated security mechanisms, it is very difficult to provide secure communication guarantees.

## Slide 10: Design choices for providing QoS
Some of the design choices for providing QoS support are described below.
Hard state versus soft state resource reservation
Stateful versus stateless approach
Hard QoS versus soft QoS approach

## Slide 11: Hard state versus soft state resource reservation
QoS resource reservation is responsible for reserving resources at all intermediate nodes along the path from the source to the destination, as requested by the QoS session.
QoS resource reservation mechanisms can be broadly classified into two categories: hard state and soft state reservation mechanisms.
In hard state resource reservation schemes, resources are reserved at all intermediate nodes along the path from the source to the destination throughout the duration of the QoS session.
In soft state resource reservation mechanisms maintain reservations only for small time intervals are used.

## Slide 12: Stateful versus stateless approach
In the stateful approach, each node maintains either global state information or only local state information, while in the case of a stateless approach, no such information is maintained at the nodes.

## Slide 13: Hard QoS versus soft QoS approach
The QoS provisioning approaches can be broadly classified into two categories: hard QoS and soft QoS approaches.
If QoS requirements of a connection are guaranteed to be met for the whole duration of the session, the QoS approach is termed a hard QoS approach.
If the QoS requirements are not guaranteed for the entire session, the QoS approach is termed a soft QoS approach.