## Slide 1: Classifications of QoS Solutions

## Slide 2: Classifications of QoS Solutions
Classification of QoS approach
Layer-Wise Classification of Existing QoS Solutions

## Slide 3: Classifications of QoS Solutions
The QoS solutions can be classified in two ways.
One classification is based on the QoS approach employed, while the other one classifies QoS solutions based on the layer at which they operate in the network protocol stack.

## Slide 4: Classification of QoS approach
As shown in below figure, several criteria are used for classifying QoS approaches.
The QoS approaches can be classified -
  based on the interaction between the routing protocol and the QoS provisioning mechanism
  based on the interaction between the network and the MAC layers
  based on the routing information update mechanism.

## Slide 5: Classification of QoS approach

## Slide 6: Based on interaction between the routing protocol and QoS provision mechanism
In this, QoS approaches can be classified into two categories: coupled and decoupled QoS approaches.
In the case of the coupled QoS approach, the routing protocol and the QoS provisioning mechanism closely interact with each other for delivering QoS guarantees. If the routing protocol changes, it may fail to ensure QoS guarantees.
In the case of the decoupled Qos approach, the QoS provisioning mechanism does not depend on any specific routing protocol to ensure QoS guarantees.

## Slide 7: Based on interaction between routing protocol and MAC protocol
In this, QoS approaches can be classified into two categories: independent and dependent QoS approaches.
In independent QoS approach, the network layer is not dependent on the MAC layer for QoS provisioning.
The dependent QoS approach requires the MAC layer to assist the routing protocol for QoS provisioning.

## Slide 8: Based on the routing information update mechanism employed
In this, QoS approaches can be classified into three categories: table-driven, on-demand, and hybrid QoS approaches.
In the table-driven approach, each node in the network maintains a routing table which aids in forwarding packets.
In the on-demand approach, no such tables are maintained at the nodes, and hence the source node has to discover the route on the fly.
The hybrid approach incorporates features of both the table-driven and the on-demand approaches.

## Slide 9: Layer-Wise Classification of Existing QoS Solutions
The existing QoS solutions can also be classified based on which layer in the network protocol stack they operate in.
Below figure gives a layer-wise classification of QoS solutions.
The figure also shows some of the cross-layer QoS solutions proposed for ad hoc wireless networks.

## Slide 10: Layer-Wise Classification of Existing QoS Solutions