## Slide 1: MAC Layer Solutions

## Slide 2: MAC Layer Solutions
Cluster TDMA
802.11e
DBASE
MACA/PR
RTMAC

## Slide 3: MAC Layer Solutions
The MAC protocol determines which node should transmit next on the broadcast channel when several nodes are competing for transmission on that channel.
The existing MAC protocols for ad hoc wireless networks use channel sensing and random back-off schemes, making them suitable for best-effort data traffic.
Real-time traffic (such as voice and video) requires bandwidth guarantees.
Supporting real-time traffic in these networks is a very challenging task.

## Slide 4: MAC Layer Solutions
In most cases, ad hoc wireless networks share a common radio channel operating in the ISM band or in military bands.
The most widely deployed medium access technology is the IEEE 802.11 standard.
The 802.11 standard has two modes of operation: a distributed coordination function (DCF) mode and a point coordination function (PCF) mode.

## Slide 5: MAC Layer Solutions
The DCF mode provides best-effort service, while the PCF mode has been designed to provide real-time traffic support in infrastructure-based wireless network configurations.
Due to lack of fixed infrastructure support, the PCF mode of operation is ruled out in ad hoc wireless networks.
Currently the IEEE 802.11 Task Group e (TGe) is enhancing the legacy 802.11 standard to support real-time traffic.

## Slide 6: MAC Layer Solutions
The upcoming 802.11e standard has two other modes of operation, namely, enhanced DCF (EDCF) and hybrid coordination function (HCF) to support QoS in both infrastructure-based and infrastructure-less network configurations.

## Slide 7: Cluster TDMA
Gerla and Tsai proposed Cluster TDMA for supporting real-time traffic in ad hoc wireless networks.
In bandwidth-constrained ad hoc wireless networks, the limited resources available need to be managed efficiently.
To achieve this goal, a dynamic clustering scheme is used in Cluster TDMA.
In this clustering approach, nodes are split into different groups.
Each group has a cluster-head (elected by members of that group), which acts as a regional broadcast node and as a local coordinator to enhance the channel throughput.

## Slide 8: Cluster TDMA
Every node within a cluster is one hop away from the cluster-head.
The formation of clusters and selection of cluster-heads are done in a distributed manner.
Clustering algorithms split the nodes into clusters so that they are interconnected and cover all the nodes.
Three such algorithms used are lowest-ID algorithm, highest-degree (degree refers to the number of neighbors which are within transmission range of a node) algorithm, and least cluster change (LCC) algorithm.

## Slide 9: Cluster TDMA
In the lowest-ID algorithm, a node becomes a cluster-head if it has the lowest ID among all its neighbors.
In the highest-degree algorithm, a node with a degree greater than the degrees of all its neighbors becomes the cluster-head.
In the LCC algorithm, cluster-head change occurs only if a change in network causes two cluster-heads to come into one cluster or one of the nodes moves out of the range of all the cluster-heads.

## Slide 10: Cluster TDMA
A frame is split into a control phase and a data phase.
In the control phase, control functions such as frame and slot synchronization, routing, clustering, power management, code assignment, and virtual circuit (VC) setup are done.

## Slide 11: Cluster TDMA
The cluster-head does the reservation for the VC by assigning the slot(s) and code(s) to be used for that connection.
In each cluster, the corresponding cluster-head maintains a power gain matrix.
The power gain matrix contains the power gain lists of all the nodes that belong to a particular cluster.
It is useful for controlling the transmission power and the code division within a cluster.

## Slide 12: Cluster TDMA
The data phase supports both real-time and best-effort traffic. Based on the bandwidth requirement of the real-time session, a VC is set up by allocating sufficient number of slots in the data phase.

## Slide 13: IEEE 802.11e
IEEE 802.11 MAC Protocol
  Distributed Coordination Function
  Point Coordination Function
Enhanced Distributed Coordination Function
Hybrid Coordination Function

## Slide 14: IEEE 802.11 MAC Protocol
The 802.11 MAC protocol describes how a station present in a WLAN should access the broadcast channel for transmitting data to other stations.
It supports two modes of operation, namely, distributed coordination function (DCF) and point coordination function (PCF).
The DCF mode does not use any kind of centralized control, while the PCF mode requires an access point (AP, i.e., central controller) to coordinate the activity of all nodes in its coverage area.
All implementations of the 802.11 standard for WLANs must provide the DCF mode of operation, while the PCF mode of operation is optional.

## Slide 15: Distributed Coordination Function
In the DCF mode, all stations are allowed to contend for the shared medium simultaneously.
CSMA/CA mechanism and random back-off scheme are used to reduce frame collisions.
Each unicast frame is acknowledged immediately after being received.
If the acknowledgment is not received within the timeout period, the data frame is retransmitted.
Broadcast frames do not require acknowledgments from the receiving stations.

## Slide 16: Point Coordination Function
The IEEE 802.11 standard incorporates an optional access method known as PCF to let stations have priority access to the wireless medium.
This access method uses a point coordinator (PC), which operates at an AP. Hence PCF is usable only in infrastructure-based network configurations.
A station which requires the PCF mode of operation sends an association message to the PC to register in its polling list and gets an association identifier (AID).
The PC polls the stations registered in its polling list in ascending order of AIDs to allow them contention-free access to the medium.
The role of the PC is to determine which station should gain access to the channel.
The stations requesting the PCF mode of operation get associated with the PC during the contention period (CP).
With PCF, the channel access alternates between the contention-free period (CFP) and the contention period (CP) for the PCF and DCF modes of operation, respectively.

## Slide 17: Enhanced Distributed Coordination Function
Enhanced distributed coordination function (EDCF) provides differentiated and distributed access to the wireless medium.
Each frame from the higher layer carries its user priority (UP).
After receiving each frame, the MAC layer maps it into an access category (AC).
Each AC has a different priority of access to the wireless medium.
One or more UPs can be assigned to each AC.
EDCF channel access has up to eight Acs, to support UPs. EDCF supports eight UPs.

## Slide 18: Hybrid Coordination Function
The hybrid coordination function (HCF) combines features of EDCF and PCF to provide the capability of selectively handling MAC service data units (MSDUs), in a manner that has upward compatibility with both DCF and PCF.
It uses a common set of frame exchange sequences during both the CP and the CFP.
The HCF is usable only in infrastructure-based BSSs that provide QoS, that is, QBSSs.
The HCF uses a QoS-aware point coordinator, called HC, which is typically collocated with a QAP.

## Slide 19: Hybrid Coordination Function
The HC implements the frame exchange sequences and the MSDU handling rules defined in HCF, operating during both the CP and the CFP.
It allocates TXOPs to stations and initiates controlled contention periods for the stations to send reservation requests.
When the HC needs access to the wireless medium, it senses the medium.
If the medium remains idle for a PIFS period, it initiates MSDU deliveries.
The HC can start contention-free controlled access periods (CAPs) at any time during a CP, after the medium is determined to be idle for at least one PIFS period.

## Slide 20: DBASE
The distributed bandwidth allocation/sharing/extension (DBASE) protocol supports multimedia traffic [both variable bit rate (VBR) and constant bit rate (CBR)] over ad hoc WLANs.
In an ad hoc WLAN, there is no fixed infrastructure (i.e., AP) to coordinate the activity of individual stations.
For real-time traffic (rt-traffic), a contention-based process is used in order to gain access to the channel.

## Slide 21: DBASE
Once a station gains channel access, a reservation-based process is used to transmit the subsequent frames.
The non-real time stations (nrt-stations) regulate their accesses to the channel according to the standard CSMA/CA protocol used in 802.11 DCF.
The DBASE protocol permits real-time stations (rt-stations) to acquire excess bandwidth on demand.