## Slide 1: Energy Management In Ad Hoc Wireless Networks
UNIT-V

## Slide 2: Syllabus
Need for Energy Management in Ad Hoc Wireless Networks
Classification of Energy Management Schemes
Battery Management Schemes
Transmission Power Management Schemes
System Power Management Schemes

## Slide 3: INTRODUCTION
The nodes in an ad hoc wireless network are constrained by limited battery power for their operation.
So, energy management is an important issue in such networks.
The use of multi-hop radio relaying requires a sufficient number of relaying nodes to maintain the network connectivity.
Hence, battery power is a precious resource that must be used efficiently in order to avoid early termination of any node.

## Slide 4: INTRODUCTION
Energy management deals with the process of managing energy resources by means of
  controlling the battery discharge
  adjusting the transmission power
  scheduling of power sources
to increase the lifetime of the nodes of an ad hoc wireless network.
Efficient battery management, transmission power management, and system power management are the three major means of increasing the life of a node.

## Slide 5: INTRODUCTION
Battery management is concerned with problems that lie in the selection of battery technologies, finding the optimal capacity of the battery, and scheduling of batteries, that increase the battery capacity.
Transmission power management techniques attempt to find an optimum power level for the nodes in the ad hoc wireless network.
System power management deals mainly with minimizing the power required by hardware peripherals of a node (such as CPU, DRAM, and LCD display) and incorporating low-power strategies into the protocols used in various layers of the protocol stack.

## Slide 6: NEED FOR ENERGY MANAGEMENT IN AWN
The energy efficiency of a node is defined as the ratio of the amount of data delivered by the node to the total energy expended.
Higher energy efficiency implies that a greater number of packets can be transmitted by the node with a given amount of energy reserve.
The main reasons for energy management in ad hoc wireless networks are-
Limited energy reserve
Difficulties in replacing the batteries
Lack of central coordination
Constraints on the battery source
Selection of optimal transmission power
Channel utilization

## Slide 7: Limited energy reserve
The main reason for the development of ad hoc wireless networks is to provide a communication infrastructure in environments where the setting up of a fixed infrastructure is impossible.
Ad hoc wireless networks have very limited energy resources.
Advances in battery technologies have been negligible as compared to the recent advances that have taken place in the field of mobile computing and communication.
The increasing gap between the power consumption requirements and power availability adds to the importance of energy management.

## Slide 8: Difficulties in replacing the batteries
Sometimes it becomes very difficult to replace or recharge the batteries.
In situations such as battlefields, this is almost impossible.
So, energy conservation is essential in such scenarios.

## Slide 9: Lack of central coordination
The lack of a central coordinator, such as the base station in cellular networks, introduces multi-hop routing and necessitates that some of the intermediate nodes act as relay nodes.
If the proportion of relay traffic is large, then it may lead to a faster depletion of the power source for that node.
If no relay traffic is allowed through a node, it may lead to partitioning of the network.
Hence, unlike other networks, relay traffic plays an important role in ad hoc wireless networks.

## Slide 10: Constraints on the battery source
Batteries tend to increase the size and weight of a mobile node.
Reducing the size of the battery results in less capacity which, in turn, decreases the active lifespan of the node.
In addition to reducing the size of the battery, energy management techniques are necessary to utilize the battery capacity in the best possible way.

## Slide 11: Selection of optimal transmission power
The transmission power selected determines the reachability of the nodes.
The consumption of battery charge increases with an increase in the transmission power.
An optimal value for the transmission power decreases the interference among nodes, which, in turn, increases the number of simultaneous transmissions.

## Slide 12: Channel utilization
A reduction in the transmission power increases frequency reuse, which leads to better channel reuse.
Power control becomes very important for CDMA-based systems in which the available bandwidth is shared among all the users.
Power control is essential to maintain the required signal to interference ratio (SIR) at the receiver and to increase the channel reusability.