## Slide 1: TRANSMISSION POWER MANAGEMENT SCHEMES

## Slide 2: TRANSMISSION POWER MANAGEMENT SCHEMES
The components used in the communication module consume a major portion of the energy in AWN.
In TPMS we investigate some of the means of achieving energy conservation through efficient utilization of transmission power such as selection of an optimal power for communication.
The variation in transmission power greatly influences the reachability of a node.
Increasing the transmission range not only increases coverage, but also the power consumption rate at the transmitter.
TPMS deals with finding a trade-off between the two contradictory issues, i.e, increasing the coverage of a node and decreasing its battery consumption.

## Slide 3: Data Link Layer Solutions
Transmitter power greatly influences the reachability of the node and thus the range covered by it.
Power control can be effected at the data link layer by means of topology control and constructing a power control loop.
In this topic we discuss different power-based solutions at the data link layer.
Recent works suggest that a proper selection of power levels for nodes in an AWN may lead to saving of power and unnecessary wastage of energy.
Some of the solutions proposed to calculate the optimum transmission range are as follows:
Dynamic power adjustment policies
Distributed topology control algorithms
Constructing distributed power control loop
Centralized topology control algorithm

## Slide 4: Dynamic Power Adjustment Based on the Link Affinity
AWN are prone to constant link failures due to node mobility, hence the stability of routes cannot be assured in such situations.
But frequent link failures lead to reduced throughput.
A parameter called affinity that decides the stability of a route.
Node m samples a set of signals from the node n and calculates the affinity (anm).
After calculating the signal strength, the node adjusts its transmission power (PT) accordingly.
Each node transmits with the minimum power that is required to reach the destination.
Thus dynamic power adjustment can be made in a distributed way.
Around 3% to 5% of power saving can be obtained using the above scheme.

## Slide 5: Distributed Topology Control Mechanisms
According to this algorithm, each node of the ad hoc wireless network independently runs a localized algorithm and decides the appropriate power level to be used by that node.
A node increases the power directionally until it finds one node in all the directions.
Then it tries to increase the lifetime of the nodes to a greater extent by reducing the transmission power and having less coverage of the nodes while guaranteeing the same connectivity as the one achieved when the nodes are maximally powered.
The principle behind this algorithm is that the topology of the network can be changed by choosing the appropriate power level.
An improper network topology may suffer from poor network utilization, lesser battery life, and higher delays.

## Slide 6: Constructing Distributed Power Control Loop
The main objective behind the algorithm is to reduce the energy cost of communication between the nodes and thereby increasing the battery lifetime and the effective bandwidth.
The main reasons behind the need for distributed algorithms in AWN are the mobility and absence of a central arbiter which can inform the nodes about the power levels to be used.
The algorithm aims at allowing each node to use different power levels while transmitting to different nodes and at the same time maintaining the connectivity of the network.
This is because nodes that are closer require less power for transmission, but on using a common power level, interference may be increased when higher power is selected as a common power level and used for communicating with nearby nodes.
The power control algorithm has been incorporated into the IEEE 802.11 MAC protocol.

## Slide 7: Constructing Distributed Power Control Loop
Thus each node calculates which level of power is to be used for transmission to each of its neighboring nodes.
Dynamic topology construction algorithm in which nodes, by overhearing the RTS-CTS packets, calculate their transmission powers.
The main aim of this power control dual channel (PCDC) protocol is to choose the transmission power in such a way that the connectivity between nodes remains unaffected but at the same time increases the number of simultaneous transmissions in the network, and thereby the throughput.

## Slide 8: Constructing Distributed Power Control Loop

## Slide 9: Centralized Topology Control Algorithm
The algorithm is a centralized algorithm which adjusts the power level of the nodes to create the desired topology.
The problem is constrained as an optimization problem with power level as the optimization objective and the constraints are connectivity and biconnectivity.

## Slide 10: Summary

## Slide 11: Network Layer Solutions
Common Power Protocol
Globalized Power-Aware Routing Techniques
  Minimum Power Consumption Routing
  Minimum Variance in Node Power Levels
  Minimum Battery Cost Routing
  Min-Max Battery Cost Routing
  Conditional Min-Max Battery Cost Routing
  Minimum Energy Disjoint Path Routing
Localized Power-Aware Routing Techniques
  Power-Saving Localized Routing (SP-Power) Algorithm
  Cost-Saving Localized Routing (SP-Cost) Algorithm
  Power-Cost-Saving Localized Routing Algorithm
Energy-Efficient Ad Hoc Wireless Networks Design Algorithm
Determination of Critical Transmission Range

## Slide 12: Network Layer Solutions
The power at the network layer can be conserved by reducing the power consumed for two main operations, namely, communication and computation.
The communication-related power consumption is mainly due to the transmit-receive module present in the nodes.
The computation power refers to the power spent in calculations that take place in the nodes during routing and power adjustments.
Hence, a balance must be reached between the number of computation and communication tasks performed by the node, which are contradictory to each other.

## Slide 13: Common Power Protocol
A common power protocol (COMPOW) that attempts to satisfy three major objectives:
  increasing the battery lifetime of all the nodes
  increasing the traffic-carrying capacity of the network
  reducing the contention among the nodes
The main reason behind the need for an optimal transmit power level for the nodes in an AWN is that battery power is saved by reducing the transmission range of the node.
This also leads to a connected network with minimum interference.
They put forth the following reasons for a common power level in an AWN:
  For the proper functioning of the RTS-CTS mechanism
  For proper functioning of link-level acknowledgments

## Slide 14: Globalized Power-Aware Routing Techniques
Minimizing the overall transmission power and distributing the power consumption evenly among the nodes are contradictory to each other.
A power optimal scheduling and routing protocol proposed which tries to minimize the total average power in the network, subjected to constraints such as peak transmission power of the nodes and achievable data rate per link.

## Slide 15: Minimum Power Consumption Routing
The total transmission power for route l is the sum of the transmission powers of all nodes in the route.
According to minimum power consumption routing (MPCR), the preferred route is the one with minimum total transmission power among all the available routes between the source and the destination.
This routing algorithm can be realized by modifying the Dijkstra’s shortest path algorithm.
But this may select a path with a greater number of hops, which passes through nodes that require less power.
Hence it may result in increasing the end-to-end delay of the packets in the network.
In addition to this, involving greater number of hops may reduce the stability of the route because of the node mobility which is one of the inherent characteristics of AWN.
Hence, the Bellman Ford algorithm is considered, which takes into account transmission power as a cost metric.
This algorithm tries to reduce the overall power consumption of the network, but still lacks in the ability to reduce the power consumed at individual nodes.
As shown in below figure, node n may be a common node used by multiple flows simultaneously. This may render node n deprived of all its battery charge faster than other nodes in the network.

## Slide 16: An illustration of the disadvantage in using shortest path routing

## Slide 17: Minimum Variance in Node Power Levels
The main motivation behind this metric is to ensure that all the nodes are given equal importance and no node is drained at a faster rate compared to other nodes in the network.
This problem is similar to the load sharing problem in distributed systems, which is an NP-complete problem.
A scheme called join the shortest queue (JSQ) that tries to attain the optimal solution.
According to this algorithm, for transmitting a packet, a node selects the next-hop node so that it has the least amount of traffic among all neighbors of the node.
The objective can also be realized by applying a round robin selection of next-hop neighbors.

## Slide 18: Minimum Battery Cost Routing
In the minimum battery cost routing (MBCR) algorithm, individual battery charges are taken into consideration while selecting the route, i.e, the path selected must not contain the nodes that have less remaining battery capacity.
The major drawback with this scheme is that the use of summation of the remaining energy of the nodes as a metric selects the path which has more remaining energy on an average for all of its nodes rather than for individual nodes.

## Slide 19: Illustrating the disadvantage of minimum-cost routing

## Slide 20: Min-Max Battery Cost Routing
The objective function of the min-max battery cost routing (MMBCR) algorithm is to make sure that route selection is done based on the battery capacity of all the individual nodes.
A variant of this routing algorithm minimizes the maximum cost after routing N packets to the destination or after a time period of t seconds.
This tries to postpone the first node failure, which ultimately leads to a longer network lifetime.
This algorithm ensures uniform discharge from the batteries.
A closer look at it reveals that the path chosen does not ensure minimum transmission power and hence rapidly reduces the lifetime of all the nodes.

## Slide 21: Conditional Min-Max Battery Cost Routing
In order to solve the contradictory issues that exist in the algorithms previously mentioned, instead of using the battery cost, conditional min-max battery cost routing (CMMBCR) considers the battery capacity directly.
A threshold value γ is defined for the remaining battery capacity of the nodes.
Only those paths that have sufficiently higher capacity for all their nodes compared to the threshold participate in the routing algorithm.
Once the competing routes are decided, the usual MTPR algorithm is applied on them so as to choose the path with minimum total transmission power.

## Slide 22: Minimum Energy Disjoint Path Routing
In this technique they have proposed minimum energy disjoint path routing for two cases: (a) node disjoint case and (b) link disjoint case.
The important need for having disjoint paths in WN, especially in AWN, is because of the need for reliable packet transmission and energy efficiency.
Ad hoc networks are highly unreliable due to the mobility of nodes and hence the probability of link failure is quite high in such networks.
This problem can be overcome by means of link disjoint routing.
Since the ad hoc nodes have stringent battery constraints, node disjoint routing considerably increases the lifetime of the network by choosing different routes for transmitting packets at different points of time.
The routing schemes assume that the topology is known a priori in the form of an energy-cost graph.

## Slide 23: Localized Power-Aware Routing Techniques
The aim of this routing protocol is to find the shortest route to the destination so as to increase the net lifetime of the power source (battery), using localized algorithms.
This protocol is based on the basic principle that, by placing intermediate nodes at the desired location between two nodes separated by a distance d, the transmission power can be made proportional to the distance d rather than dα, where α ≥ 2.
The protocol tries to find the route that minimizes the total power needed, which increases the battery lifetime.

## Slide 24: Power-Saving Localized Routing (SP-Power) Algorithm
The power-saving localized routing algorithm from source S to destination D is given below.
Step 1: Let A := S.
Step 2: Let B := A.
Step 3: Each node B, which may be a source or intermediate node, will select one of its neighbors A so as to minimize the power p(B, A)=u(r) + tv(s) and sends the message to neighbor node A.
Step 4: Steps 2 and 3 are repeated until the destination is reached, that is, A = D, or the delivery has failed, in which case A = B.

## Slide 25: Cost-Saving Localized Routing (SP-Cost) Algorithm
The cost-saving localized routing algorithm from source S to destination D is given below.
Step 1: Let A := S.
Step 2: Let B := A.
Step 3: Let each node B, which may be a source or intermediate node, select the neighbor node A that minimizes the cost c(A). If node D is one of the neighbors, send the message to node D, else send it to node A.
Step 4: Steps 2 and 3 are repeated till the destination is reached, that is, A = D, or the delivery has failed, in which case A = B.

## Slide 26: Power-Cost-Saving Localized Routing Algorithm
Depending on which factor is used, either sum or product, the power-cost-saving localized routing algorithm from source S to destination D can be represented as SP-Power*Cost or SP-Power+Cost algorithm.
Step 1: Let A := S.
Step 2: Let B:= A.
Step 3: Let each node B, which may be a source or intermediate node, select the neighbor node A that minimizes the value pc(B, A) = power-cost(B, A) + v(s)f´ (A). Send the message to A.
Step 4: Steps 2 and 3 are repeated till the destination is reached, that is, A = D, or the delivery has failed, in which case A = B.

## Slide 27: Energy-Efficient Ad Hoc Wireless Networks Design Algorithm
An energy-efficient network design algorithm called ad hoc network design algorithm (ANDA), which tries to maximize the network lifetime for a static network where cluster-heads are known a priori.
The basic idea used in this protocol is that the cluster-heads dynamically adjust the power level; and hence, the cluster size varies based on the remaining battery charge.
Thus energy is uniformly drained from the cluster-heads, which in turn increases the lifetime of the network.

## Slide 28: Determination of Critical Transmission Range
A centralized algorithm calculates the minimum power level for each node that is required to maintain network connectivity based on the global information from all the nodes.
This minimum value of the node’s transmission range is termed the critical transmission range.
This algorithm aims at finding the transmission range for each of the nodes which acts as a tradeoff between increasing the network connectivity, the spatial reusability, and the battery-life extension.
The optimal value of the reception range depends on the following factors: Mobility, Propagation models, Power level, Antenna configuration.

## Slide 29: Network Layer Solutions

## Slide 30: Network Layer Solutions

## Slide 31: Network Layer Solutions

## Slide 32: Higher Layer Solutions
Here some of the power-aware techniques handled at the TCP/IP and the application layers of the protocol stack.
The protocols used at these layers incorporate in them power control and energy conservation.

## Slide 33: Congestion Control and Transmission Policies at the TCP/IP Layer
Due to the mobile nature of AWN and the absence of the central coordinator such as a base station, the links are highly error-prone, which results in a large number of retransmissions, which in turn constantly invokes congestion control mechanisms.
This kind of a situation is highly intolerable in the case of AWN because of the limited energy source.
Protocols at the TCP layer have to take into account the energy reserve while allowing retransmissions.
Some of the suggestions made are listed below.

## Slide 34: Congestion Control and Transmission Policies at the TCP/IP Layer
The number of retransmissions can be considerably reduced by making a few modifications in the error-control protocols at the TCP/IP layer, such as selective retransmissions and explicit loss notification (ELN), which try to differentiate between congestion and other types of losses.
Error correlation greatly affects the energy conservation of AWN. TCP layer protocols that take into consideration error bursts and backing off, which result in energy efficiency of the system, can be used.
If the packets are not received, a probe cycle may be initiated by exchanging some probe messages with the transmitter rather than using congestion control algorithms directly. This achieves higher throughput while consuming less energy due to reduced traffic in the network.

## Slide 35: OS/Middleware and Application Layer Solutions
At the application layer, protocols such as advanced configuration and power interface (ACPI) and power management tools such as power monitor are developed to assist programmers in creating power-efficient applications.
Using proxy servers results in traffic redirection or reduction in traffic, such as in multimedia where video quality may be scaled down and audio sent, and in redirecting local traffic when it arrives along with the network traffic.
This results in a huge amount of energy conservation.
Some energy-conserving metrics can also be used in database design such as energy per transaction.
In the context of multimedia, energy conservation can be achieved by reducing the number of bits in the compressed video and by transmitting only selected information.
Multimedia traffic consumes a large amount of energy in AWN systems.