## Slide 1: System Power Management Schemes

## Slide 2: System Power Management Schemes
Processor Power Management Schemes
  Power-Saving Modes
  Power-Aware Multi-Access Signaling
    Addition of separate signaling channel
    Powering off the radios
Device Power Management Schemes
  Low-Power Design of Hardware
    CPU Power Consumption
    Power-Aware CPU Scheduling
    Hard Disk Drive (HDD) Power Consumption

## Slide 3: System Power Management Schemes
SPMS deals with power control in the peripherals and the processor of nodes in an AWN.
Efficient design of the hardware brings about significant reduction in the power consumed.
This can be effected by operating some of the peripheral devices in power-saving mode by turning them off under idle conditions.
System power consists of the power used by all hardware units of the node.
This power can be conserved significantly by applying the following schemes:
  Processor power management schemes
  Device power management schemes

## Slide 4: Processor Power Management Schemes
Processor power management schemes deal with techniques that try to reduce the power consumed by the processor, such as reducing the number of calculations performed.
Some of the power management techniques that are applied at the hardware level when there is a request from the higher layers are –
  Power-Saving Modes
  Power-Aware Multi-Access Signaling

## Slide 5: Power-Saving Modes
The nodes in an AWN consume a substantial amount of power even when they are in an idle state since they keep listening to the channel, awaiting request packets from the neighbors.
In order to avoid this, the nodes are switched off during idle conditions and switched on only when there is an arrival of a request packet.
This primarily has two advantages: reducing the wastage in power consumed when the node is in the listen mode, and providing idle time for the batteries of the node to recover charges.
Since the arrival of request packets is not known a priori, it becomes difficult to calculate the time duration for which the node has to be switched off.

## Slide 6: Power-Saving Modes
One solution to this problem is calculate the node’s switch-off time based on the quality of service (QoS) requirements.
An assumption made in these systems is that the battery subsystem of the node can be remotely powered on by means of a wake-up signal that is based on RF tag technology.
RF tags are used as transponders for remote localization, activation, and identification of objects within a short range.
Hard QoS requirements make the node stay active most of the time.
This results in high consumption of the battery charge.

## Slide 7: Remote activated switch

## Slide 8: Power-Aware Multi-Access Signaling
Power-aware multi-access signaling (PAMAS) is another approach for determining the time duration for which the node should be turned off.
This scheme suggests the addition of a separate signaling channel in the MACA protocol.
The RTS-CTS signaling takes place in this separate channel, which determines the time period for which the node has to be powered off.
The algorithm is divided into two parts:
  Addition of separate signaling channel
  Powering off the radios

## Slide 9: Addition of separate signaling channel
A node can be in any one of the six states represented within the boxes.

## Slide 10: Addition of separate signaling channel
Initially, when a node neither transmits nor receives packets, it stays in the idle state.
Packet transmission -
  As soon as the node gets a packet for transmission, it transmits an RTS and enters the Await CTS state.
  If it does not receive the CTS, it enters the binary exponential back-off (BEB) state. A node also enters the BEB state if it hears a busy tone when a neighboring node which is actively transmitting sends a busy tone in the control channel.
  After receiving the CTS, it enters the Transmit packet state and starts transmitting the packet.

## Slide 11: Addition of separate signaling channel
Packet reception -
  As soon as a node receives an RTS, it sends a CTS back to the sender and enters the Await packet state, only if no other neighboring nodes exist in the Await CTS or Transmit packet state.
  If packets arrive on time, the node enters the Receive packet state and starts receiving the packets.
  If the packet does not arrive on time, the node enters the idle state again.

## Slide 12: Powering off the radios
The conditions under which the node enters the power-off mode is :
  Condition 1: The node has no packets for transmission.
  Condition 2: A neighbor node is transmitting or receiving packets, i.e, the channel is busy.

## Slide 13: Device Power Management Schemes
Some of the major consumers of power in AWN are the hardware devices present in the nodes.
Various schemes have been proposed in the design of hardware that minimize the power consumption.

## Slide 14: Low-Power Design of Hardware
Low-power design of hardware results in a significant improvement in the energy conservation.
Some of the low-power design suggestions include varying clock speed CPUs, disk spin down, and flash memory.

## Slide 15: Low-Power Design of Hardware
Some of the sources of power consumption in the AWN and the corresponding solutions to reduce power consumption are –
  Major sources of power consumption in AWN are the transmitters and receivers of the communication module. The design of transceivers has a significant effect on the power consumption. Hence, great care must be taken while designing them. Switching off various units of the hardware while idling reduces the energy consumption. Instead of switching off fully, different stages may be followed in each of which there exists a different power requirement.
  The main hardware of a mobile node consists of the LCD display, DRAM, CD ROM drive, CPU, wireless interface card (in the case of a computer), and I/O subsystems.
  The percentage of power consumed by some of these components is shown in below figure -

## Slide 16: Power consumed by various units of hardware

## Slide 17: CPU Power Consumption
The energy required for the CPU operation depends largely on the clock frequency (F).
As the clock rate increases, frequent switching of the logic gates between different voltage levels (V), i.e, the ground voltage and the peak voltage, takes place, which leads to higher power consumption.
Another effect that significantly influences the CPU power consumption is the chaining of transistors.
The larger the capacitance (C) of these transistors, the higher the energy required.
The total power required by the CPU is proportional to CV^2F.
The solution suggested is as follows:
  The parameter C can be set during the chip design.
  The values of F and V can be set dynamically at run-time which, along with power-aware CPU scheduling policies, reduces the power consumption significantly.

## Slide 18: Power-Aware CPU Scheduling
A small reduction in the value of the voltage V produces a quadratic reduction in the power consumed.
This is the motivation behind the power-reduction techniques.
But the voltage V cannot be reduced until the clock rate is reduced.
The CPU utilization can be balanced between peak usage and idle periods.
Idle periods or sleep times can be classified into hard or soft sleep times.
Hard sleep times are unavoidable and result in compulsory idle times, whereas the soft idle times are those which can be delayed to a maximum extent possible.
These two kinds of sleep times must be taken into account while balancing the CPU activities.

## Slide 19: Hard Disk Drive (HDD) Power Consumption
The basic source for power consumption in hard disks is the disk spin.
Various approaches have been suggested for turning off the drives and to bring down the speed of spinning.
The spin-down can be performed on the disk drives by using historical data or by Spin-up/spin-down policies(Optimal-optimal policy, Threshold-demand policy, Predictive-predictive policy).

## Slide 20
SUMMARY

## Slide 21
END OF UNIT-V