## Slide 1: UNIT-VI
Recent Advances in Wireless Networks

## Slide 2: Syllabus
Ultra-Wide-Band Radio Communication
Wireless Fidelity Systems
Optical Wireless Networks
The Multimode 802.11 – IEEE 802.11a/b/g
The Meghadoot Architecture

## Slide 3: Introduction
In order to support high data rates on short ranges, new promising technologies such as the ultra-wide band (UWB) transmission scheme and optical wireless wavelength division multiplexing (WDM) networks are currently under research.
In addition to the demands on increasing the performance of the lower layers of the system, pressure is on to efficiently reuse the existing frequencies, which also demands allocation of newer bands for commercial wireless communications.
The additional areas of interest in next-generation wireless networks include freedom in selection of a particular network from a set of heterogeneous wireless networks, seamless handoff across such networks, support for multimedia traffic, and all the above services at an affordable cost.

## Slide 4: Introduction
The first step in this is the development of wireless fidelity (Wi-Fi) systems that integrate the high-speed wireless LANs with the wide-area packet cellular infrastructure.
The demand for high bandwidth for high-quality multimedia traffic has also resulted in utilizing the WDM technology in wireless communication.

## Slide 5: ULTRA-WIDE-BAND RADIO COMMUNICATION
Operation of UWB Systems
A Comparison of UWB with Other Technologies
Major Issues in UWB
UWB Applications
Advantages and Disadvantages of UWB

## Slide 7: Spectrum of UWB systems compared with IEEE 802.11b and 802.11a

## Slide 8: Operation of UWB Systems
The operation of UWB systems is based on transmission of ultra-short pulses which are also called monocycles.
Each monocycle is similar to a single cycle of an ultra-high-frequency sine wave and is a single ultra-short pulse.
The pulse widths of monocycles range from 0.10 to 1.6 ns with pulse-to-pulse intervals of between 25 and 1,000 ns.
A single monocycle of width 0.5 ns is shown in Figure (a).
Figure (b) shows a pulse train involving a sequence of monocycles generated at regular intervals.
Monocycles are inherently wide bandwidth signals.

## Slide 9: An illustration of a monocycle and pulse train

## Slide 10: A Comparison of UWB with Other Technologies
The trends that drive the short-range wireless technologies, including UWB technology, are the following:
  The growing demand for data and multimedia capability in portable devices at high data rate but at low cost and power consumption.
  Increasing pressure on the wireless spectrum demanding higher reuse.
  Decreasing semiconductor cost and availability of low-power devices.
Some of the competing technologies for such wireless access scenario are IEEE 802.11b, IEEE 802.11a, and Bluetooth.
The bandwidth, transmission range, and capacity comparison in bps/m2 among 802.11b, Bluetooth, 802.11a, and UWB is illustrated in below figures.

## Slide 11: Bandwidth comparison of UWB with other competing technologies

## Slide 12: Range comparison of UWB with other competing technologies

## Slide 13: Capacity comparison of UWB with other competing technologies

## Slide 14: Major Issues in UWB
With the evolution of wireless networks with higher data rates, similar advancement in all the layers of protocol stack is required to make use of the high data rates provided by the physical layers.
The increasing application space for multimedia communications puts additional requirements on latency and delay performances.
The error-prone and time-varying nature of wireless link results in large delay, delay variations, and misordering of packets.

## Slide 15: Physical Layer
The wide-band receiver used for the UWB system is susceptible to being jammed by the traditional narrow band that operates within the UWB pass band.
Issues such as the wide bandwidth required for the filters and antenna subsystems and filter-matching accuracy are major physical-layer issues difficult to solve without adding to the cost of the physical-layer interface.
At the receiver, accurate timing is required for detecting the modulated narrow pulses accurately.
In addition to all the above, noise from the on-board micro-controller can also result in interference that cannot be easily solved using traditional mechanisms such as band-pass filters, due to the wide bandwidth of the system.

## Slide 16: MAC Layer
The most important issues in the design of MAC-layer protocol for UWB systems are the following:
(i) controlling channel access
(ii) maintaining QoS
(iii) providing security
In addition to these, the design of MAC protocols for UWB systems is dictated by other properties of UWB.

## Slide 17: UWB Applications
Promising applications of UWB in communication include cable-free audio/video devices, broadband WPANs, and high-speed wireless links.
UWB systems are potential candidates for high data rate, low power, and short- to medium-range communication applications.
UWB systems have a wide range of applications other than communications, some of which are automobile collision-detection devices, medical imaging similar to x-rays and ultrasound scans, through-wall imaging for detecting people and objects in law-enforcement applications, and ground-penetrating radars in construction applications.

## Slide 18: UWB Advantages and Disadvantages
Advantages-
  The major advantages of UWB systems include simplicity of implementation, high data rate, inherent robustness to multipath fading, flexibility of operation, low power consumption, and low cost of implementation.
Disadvantages-
  The disadvantages of UWB systems include stringent design requirements of communication subsystems and chances of interference from the existing technologies.