## Slide 1: WIRELESS FIDELITY SYSTEMS

## Slide 2: WIRELESS FIDELITY SYSTEMS
The Service Provider Models for Wi-Fi Systems
Issues in Wi-Fi Systems
Interoperability of Wi-Fi Systems and WWANs
Pricing/Billing Issues in Wi-Fi Systems

## Slide 3: WIRELESS FIDELITY SYSTEMS
Wireless fidelity (Wi-Fi) system is the high-speed wireless LAN that was originally intended to extend the wired Ethernet in offices to wireless clients.
The coverage area and ability to support high bit rates are the two major reasons behind the name Wi-Fi.
Though the popular wireless LAN standards IEEE 802.11b and 802.11a are considered as the standard Wi-Fi candidates, conceptually any high-speed wireless LAN protocol such as HiperLAN can be used.
The integration of Wi-Fi hotspots (wireless LAN access points) with wide area wireless networking technologies such as GSM and GPRS provides an added advantage for the mobile nodes.
Such an integrated system provides secure, reliable, and high-speed wireless connectivity.

## Slide 4: WIRELESS FIDELITY SYSTEMS
A Wi-Fi network can be used to connect computers to each other, to the Internet, and to wired networks.
Wi-Fi networks operate in the unlicensed 2.4 GHz and 5 GHz radio bands, with an 802.11b or 802.11a, or with products that contain both bands (dual band), so that they can provide an enriched network experience.
Wi-Fi systems are potential candidates for provisioning high-speed multimedia content delivery in areas such as indoor offices, airport lounges, and shopping malls.
The advantages of Wi-Fi systems are ease-of-use, high-speed Internet access, low cost of operation, and flexibility of reconfiguration.

## Slide 5: The Service Provider Models for Wi-Fi Systems
The Wi-Fi micro carrier model
The franchisee-franchisor model
The Wi-Fi carrier model
The Wi-Fi aggregator model
The extended service provider model

## Slide 6: The Wi-Fi micro carrier model
In this model, small business operators can set up their own access points (APs) and maintain customer relations and billing with subscribers.
An example of this category is a restaurant operating a small Wi-Fi system with a set of APs on its premises.

## Slide 7: The franchisee-franchisor model
This model for Wi-Fi systems is that a franchisor company making an agreement with a franchisee (e.g., a restaurant which has an inbuilt Wi-Fi system for its internal purposes) for providing Wi-Fi connectivity on a revenue-sharing basis.
The external communication, access network costs, and back-office softwares may be supplied and maintained by the franchisor.
Hence, the franchisor company can extend its services to the public.

## Slide 8: The Wi-Fi carrier model
In this model, a particular company referred to as Wi-Fi carrier can own, deploy, and operate a number of Wi-Fi system enabled APs at public places.
The subscribers can utilize the designated carrier’s network services in their coverage area based on acceptable billing models.

## Slide 9: The Wi-Fi aggregator model
This model refers to an abstract service provider which strikes wholesale partnerships with Wi-Fi operators.
Such aggregators mainly focus on two major things:
  (i) reselling of the services provided by the Wi-Fi operators
  (ii) giving their subscribers access to a large number of networks.
The advantages of this model are easy scale-up of network coverage as the aggregator does not own the infrastructure and hence, by having more partnerships, a service provider can increase the coverage area and the customer base.

## Slide 10: The extended service provider model
The synergistic operation of Wi-Fi systems with existing cellular systems, especially with the 3G systems, can increase profits for cellular operators.
This can even lead to reduction in the deployment cost of 3G systems.
The widespread deployment of Wi-Fi systems can be considered as complementing the 3G systems.
Also, the availability of wireless devices equipped with Wi-Fi and cellular interfaces encourages the possibility of switching to the Wi-Fi systems whenever an AP is detected.

## Slide 11: Issues in Wi-Fi Systems
The major issues in Wi-Fi systems are the following:
  Security
  Authentication
  Quality of Service (QoS)
  Economics of Wi-Fi

## Slide 12: Security
The IEEE has proposed a long-term security architecture for 802.11, which is referred to as robust security network (RSN).
The major objectives of RSN, which is based on IEEE 802.1x, are access control, authentication, and key management.
In the infrastructure mode of operation of 802.11 standard, a client has to establish a relation with an AP called an association.
There are three main states in the transition process of an association. These are
  (i) unauthenticated and unassociated
  (ii) authenticated and unassociated
  (iii) authenticated and associated2

## Slide 13: Security
The major elements in a Wi-Fi system that can contribute to its vulnerability are –
  The eavesdropper
  The rogue client
  The rogue AP
The two major types that make a Wi-Fi network particularly vulnerable are session hijacking and man-in-the-middle attack.
Both exploit the authentication process.

## Slide 14: Authentication
The IEEE 802.1x standard is proposed for providing authentication and controlling traffic to a protected network, as well as for dynamically changing encryption keys.
The use of the extendible authentication protocol (EAP) as a framework for wired and wireless network provides a mechanism for multiple authentication methods such as certificate-based authentication, Kerberos authentication method, token cards, one-time passwords, and public key authentication.

## Slide 15: Quality of Service (QoS)
Provisioning of QoS is important in supporting time-sensitive traffic such as voice and video.
The IEEE 802.11e standard which is under consideration is aiming at providing enhanced QoS for Wi-Fi systems.

## Slide 16: Economics of Wi-Fi
Billing schemes
Revenue sharing model
Spectrum Issues

## Slide 17: Billing schemes
The entity that has the responsibility of customer care and billing can be different from the one which actually provides network access service.
Such an agency is referred to as a billing agency.
The billing agency can employ different methods to accept payments from the customers.
The major billing approaches that can be employed in the case of Wi-Fi systems are flat-rate schemes and volume based pricing.
  In flat-rate schemes, the user is permitted to utilize network services for a specified amount of time without restricting the bandwidth.
  The volume-based approach charges the customer based on the amount of data transacted over the network.

## Slide 18: Revenue sharing model
In the franchisee-franchisor model and the aggregator model, the sharing of revenue is important as there exist multiple business entities in the process of customer relationship, billing, and providing service.
Different revenue-sharing models that include a fixed fraction sharing model (in which the amount shared among the parties involved is prefixed) and a variable-fraction volume-based sharing model (in which the percentage of revenue that goes to different parties involved varies with the volume of data transferred) can be employed.
Such systems can consider a constant-fraction for the user per bit of data transferred, and in the high traffic-density environments, a variable rate per bit of data transferred can be used.
In the variable-fraction per bit of data transferred, application level mechanisms which communicate the cost of communication at any particular location is essential.

## Slide 19: Spectrum Issues
The issues related to spectrum management are important as Wi-Fi becomes popular with its increasing use as a critical business communication infrastructure.
The current allocation of free ISM band in the 2.4 GHz band for 802.11b raises several questions of interference.
The source of interferences can be either naturally generated by other devices that are designated to operate at the same band or artificially generated by a rogue interference generator node.
Since ISM band is unlicensed, any user with an 802.11 interface can disrupt communication at a specific location without inviting prosecution.

## Slide 20: Spectrum Issues
The major interference sources for Wi-Fi systems are the following:
  (i) interference from cordless phones, microwave ovens, and Bluetooth enabled devices
  (ii) interference from jammers
The first issue can be reduced to some extent by the following ways:
  (i) use of different frequency-hopping patterns for communication-technology-related interference as used in Bluetooth standard
  (ii) proper electromagnetic shielding in devices using microwave band for noncommunication-related purposes such as microwave ovens.

## Slide 21: Interoperability of Wi-Fi Systems and WWANs
The wireless wide area networks (WWANs) use base stations (BSs) that cover a few tens of kilometers in radius.
Traditionally, the mobile nodes (MNs) communicated only through these BSs.
However, WWANs provide only low bandwidth (in terms of tens of Kbps) compared to the broadband LAN services (in terms of tens of Mbps) offered by the Wi-Fi networks.
Many situations where a WWAN cannot serve the requirements well, some of which are the following: (a) interiors of buildings, basements of buildings, subways, and where the signal-to-noise ratio (SNR) may not be sufficient to provide a high-quality service (b) heavily loaded BSs (cells), where the call blocking ratio is high due to the high offered traffic and the limited spectrum of WWAN.

## Slide 22: Interoperability of Wi-Fi Systems and WWANs
The Wi-Fi operators can leave the responsibilities such as billing, brand-building, and advertising to the WAN SP and hence, the Wi-Fi SPs are likely to derive a sustained revenue at a low cost.
Hence, the interoperability between heterogeneous networks, especially between the existing WWANs and Wi-Fi networks, is mutually beneficial.
The growing deployment of Wi-Fi hotspots also underlines the importance of using them as a complementary access system to the existing WWANs.
The concentration of hotspots is especially high in places such as commercial complexes, business districts, airports, and educational institutions.

## Slide 23: Interoperability of Wi-Fi Systems and WWANs
In such scenarios, an MN currently registered with a WWAN BS may enter the coverage regions of Wi-Fi APs very frequently.
The MN may then choose to relinquish its connection to the WWAN BS and instead use the Wi-Fi AP for communication.
This leads to a reduction in the load on the cellular network, thus enabling more MNs to be supported.
The interoperability of Wi-Fi systems and cellular networks is advantageous to both the network users and the network service providers.

## Slide 24: Pricing/Billing Issues in Wi-Fi Systems
Pricing/billing schemes for a Wi-Fi systems assume significance as the commercial viability is very important for the survival of Wi-Fi systems.
In the case of Wi-Fi systems the entity that has the responsibility of customer care and billing can be different from the one which actually provides network access service.
Henceforth, the agency that is responsible for providing customer care, billing, and revenue-sharing is referred to as the billing agency (BA).

## Slide 25: Billing Agency Models
The two main aspects in any network access are the actual network service provisioning and billing.
These two were carried out by the same agency.
In Wi-Fi systems, there can be different models for the BA and the network service providers (SPs).
The basic BA models are the following:
(a) billing-free service model
(b) associated BA model
(c) revenue-sharing-based BA model
(d) integrated BA model
(e) independent BA model

## Slide 26: Billing-free service model
This is the simplest model and is in existence today in most places.
Here, the WAN BA charges MNs for their network access whereas the Wi-Fi access is provided as a free service to the users, or as a value addition to the Wi-Fi SP’s existing core business service.

## Slide 27: Associated BA model
In this case, Wi-Fi systems and WANs have independent BAs, each charging the MNs for their respective network services provided.

## Slide 28: Revenue-sharing-based BA model
This model provides a single-point billing for the MNs, and at the same time enables the MNs to avail network services from WAN or Wi-Fi networks.
A revenue-sharing agreement must be in place between the WAN BA and the Wi-Fi SPs.
Since the WAN SPs cover a larger geographical area, it is more appropriate to have the BA closely associated with the WAN SP.

## Slide 29: Integrated BA model
This model is the one that is associated with the extended service providers who operate a range of different networks including WANs and Wi-Fi APs.

## Slide 30: Independent BA model
In this case, the BA is an independent entity that has billing tie-ups with several WAN SPs and Wi-Fi SPs.