## Slide 1: Optical Wireless Networks

## Slide 2: Optical Wireless Networks
Short-Range Infrared Communication
Optical Wireless WDM
Optical Wireless WDM LAN
  Issues in OWWDM LANs

## Slide 3: Optical Wireless Networks
Optical wireless communication enables communication using infrared rays and light waves operating at frequencies well beyond the visible spectrum for high data rate local communication.
The advantages of optical wireless communication include significantly less interference due to its lack of penetration through walls, positioning of spectrum at a completely unregulated and unlicensed band, increased security, and high data rate.

## Slide 4: Optical Wireless Networks
Optical wireless technology promises broadband data delivery at short ranges in point-to-multipoint LANs and point-to-point medium-distance optical links.
Optical wireless transmission can be classified into short-range communication and long-range communication systems.
A comparison of these two types of optical wireless transmission schemes is given in below table.

## Slide 5: A comparison of optical wireless technologies

## Slide 6: Optical Wireless Networks
Long-range communication systems are mainly used for outdoor point-to-point optical links and short-range systems are used in indoor and outdoor applications.
The long-range optical wireless systems can operate over a distance of hundreds of meters only.
The short-range systems operate over a distance of few meters.

## Slide 7: Short-Range Infrared Communication
Infrared Data Association (IrDA) has developed standards that work on widely ranging data transfer rates (9.6 Kbps – 4 Mbps).
The indoor short-range communication can be classified into
  (i) Directed transmission
  (ii) Diffusion-based transmission
In directed transmission, the transmitter and receiver are required to be pointed to each other and there should exist a line of sight (LoS) transmission link between them.
In diffusion-based transmission, the transmitter and receiver need not have a LoS for communication.

## Slide 8: A comparison of two short-range transmission schemes

## Slide 9: Optical Wireless WDM
The wavelength division multiplexing (WDM) is a method of sending many light beams of different wavelengths simultaneously down the core of an optical fiber.
Operating on the basis of the WDM technology, an optical wireless network utilizes different wavelengths between a point-to-point wireless link.
This enables carrying large number of simultaneous sessions across a sender-receiver pair.
First-generation point-to-point wireless WDM systems with four wavelengths, each carrying a data rate of 2.5 Gbps, make a total transfer rate of 10 Gbps.

## Slide 10: An illustration of the wireless optical WDM point-to-point link

## Slide 11: Optical Wireless WDM
Optical wireless WDM technology is expected to increase the bandwidth to a greater extent over the wireless technologies.
It has several disadvantages, some of which are
  (i) LoS link break can lead to the loss of a tremendous amount of data
  (ii) dense smoke, rain, birds, kites, and other atmospheric changes can lead to link breaks
Reliability is one of the major design objectives for designing wireless optical WDM networks.

## Slide 12: Optical Wireless WDM
Below figure illustrates an optical wireless metro area ring network formed by several optical wireless point-to-point links.
In cities where laying of fibers is difficult or expensive, optical wireless rings are suitable alternatives.

## Slide 13
An illustration of the wireless optical WDM ring network.

## Slide 14: Optical Wireless WDM LAN
The multi-party communication in a wireless LAN environment using the radio spectrum can be replaced with the optical wireless WDM (OWWDM) system that can provide a much higher bandwidth with reduced interference and high wavelength reusability.
Below table compares the RF wireless LANs and OWWDM wireless LANs.
An illustration of the operation of OWWDM LAN is shown in below figure.
Here the stations can connect to the OWWDM AP (access point) using the control wavelength (λC) and obtain any data wavelength (λi where i = 1, 2, . . .,N) for data transfer.
This necessitates wavelength tuning capabilities at the stations and the ability to operate over multiple wavelengths at the APs.

## Slide 15: RF wireless LANs versus OWWDM wireless LANs

## Slide 17: A conceptual illustration of OWWDM LAN

## Slide 18: Issues in OWWDM LANs
The major issues in a practical OWWDM LAN include the choice of the protocols and subsystems.
MAC protocols for optical fiber LANs that belong to the category of broadcast-and-select can be extended to work in OWWDMs also.
Additional capabilities such as wavelength conversion and tuning are required for the operation of OWWDM.
The factors affecting the performance of such a system are path loss, interference, receiver sensitivity, and protocol efficiency.
In addition to all other technical issues, safety issue assumes significance in the design due to the fact that high optical energy in the specified optical bands can damage human eyes.