## Slide 1: The Multimode 802.11 – IEEE 802.11a/b/g

## Slide 2: The Multimode 802.11 – IEEE 802.11a/b/g
Multimode 802.11 is the WLAN client interface implementation that can seamlessly work with APs operating according to any of the three IEEE 802.11 standards.
At any given time, an IEEE 802.11a/b/g interface works with only one AP.
The major advantage of multimode 802.11 is the backward compatibility of the newer 802.11a and 802.11g with the millions of existing 802.11b installations.
In addition to the interoperability issue, the use of 802.11a and 802.11b simultaneously at a given service area can actually increase the available bandwidth.

## Slide 3: Comparison of bandwidth in multimode 802.11 systems
Above table provides the total bandwidth available at any given service area by the combination of 802.11a, 802.11b, and 802.11g.
The entire bandwidth may not be available for single station as it requires several network interface cards and APs.

## Slide 4: The Multimode 802.11 – IEEE 802.11a/b/g
The multimode WLAN clients that are 802.11a/b/g compatible can connect to any 802.11 AP transparently, leading to enhanced roaming services across different networks.
An 802.11a/b/g client that detects carriers from different APs using 802.11b, 802.11a, and 802.11g is illustrated in below figure.
The 802.11a/b/g client searches for carrier in all the bands of operation and selects the most appropriate one.
Hence, the new generation of wireless LAN clients are expected to be capable of operating in all these different modes, requiring a wide frequency tuning range (2 GHz to 6 GHz), multiple MAC implementations, and multiple baseband processors.

## Slide 5: The Multimode 802.11 – IEEE 802.11a/b/g

## Slide 6: The Multimode 802.11 – IEEE 802.11a/b/g
A multimode LAN client is designed to automatically select the strongest detected carrier.
A schematic diagram of the 802.11a/b/g client interface is shown in below figure.
The major difference between this interface card and the traditional single-mode client interface is the presence of multiple chipsets that can process the physical layer information belonging to different 802.11 variants.
It is necessary to have at least two such physical layer chipsets — one for the 2.4 GHz frequency range and the other for the 5 GHz frequency range to handle 802.11a/b/g physical layers.

## Slide 7: Multimode 802.11 - Schematic diagram of the multimode 802.11 client interface

## Slide 8: THE MULTIMODE 802.11 — IEEE 802.11a/b/g
The control signals from the baseband controller are used to switch to one particular physical layer chipset depending on the availability and signal strength from the APs.
In addition to the switching decisions, the baseband module includes the MAC implementations and the interfaces to the PC bus standards such as PCI, mini-PCI, and CardBus.

## Slide 9: Software Radio-Based Multimode Systems
Software-defined radio (popularly known as software radio) is a proven technology in military wireless communication systems.
In a software-defined radio system, the different modules of a radio interface such as IF (intermediate frequency), base band, and bit stream processors are implemented through general-purpose programmable digital signal processors (DSPs).
Hence such programmable, multimode, and multiband radio interfaces can provide low-cost terminals that can operate across several different networks.

## Slide 10: Software Radio-Based Multimode Systems
Below figure shows an illustration of a software-defined multimode and multiband wireless network interface operating across a GSM network and a W-CDMA network, by downloading network specific waveform software.
Every network is assumed to be using a control protocol or a control channel with the necessary information about the waveform software.
In the presence of a new network, the multimode interface detects the network over the control channel and downloads the waveform software and the necessary protocol software.
Once the new waveform and associated protocol software are loaded onto the radio interface, the mobile terminal becomes ready to communicate with the network similar to any other single-mode interface designed for that network.

## Slide 11: An illustration of operation of software-defined multimode wireless client

## Slide 12: Software Radio-Based Multimode Systems
Even though software radio is currently used at the BSs only, recent developments are aimed at using it at the terminal side also.
The major constraints for achieving this are processing power and power consumption.
Experimental software radio-based terminals that operate in dual mode between GSM and W-CDMA exist today.
They consume higher amounts of power for operation compared to the existing single-mode terminals.
With the development of high-speed processors and low-power VLSI devices, multimode terminals based on software radio may soon become a reality.