## Slide 1: The Meghadoot Architecture

## Slide 2: The Meghadoot Architecture
The Meghadoot architecture is a packet-based wireless network architecture for low-cost rural community networks.
Packet-based radio networks are considered as an ideal alternative for low-cost community networks, both in the urban developed environments and also in the rural regions.

## Slide 3: The Meghadoot Architecture
The major objectives of the Meghadoot project are
  (i) to develop a fully distributed packet-based hybrid wireless network that can carry voice and data traffic
  (ii) to provide a low-cost communication system in the rural regions
  (iii) to provide an alternate low-cost communication network for urban environments

## Slide 4: The Meghadoot Architecture
Meghadoot uses a routing protocol called infrastructure-based ad hoc routing protocol (IBAR).
An illustration of routing process in the Meghadoot architecture is shown in below figure.
The infrastructure node (IN) controls the routing process in its k-hop neighborhood (also referred to as k-hop control zone) and aids in routing for the calls originated beyond k-hops and destined to a node within the k-hop region.
Any node registered to the IN assumes that the routing and other control activities would be taken care of by the IN, and hence it stays away from initiating its own path-finding process.

## Slide 5: The Meghadoot Architecture

## Slide 6: The Meghadoot Architecture
Nodes that are not under the control of the IN operate in the ad hoc mode, and hence are required to perform self-organization, path-finding, and path reconfiguration by themselves.
The region beyond the k-hop neighborhood from an IN is called the ad hoc routing zone.
Meghadoot requires the gateway nodes (GNs) to hold the additional responsibility of interfacing the nodes in the ad hoc routing zone (operating in the ad hoc mode) to the IN in order to enable such nodes to find routes efficiently to the nodes inside the control zone of the IN.

## Slide 7: The Meghadoot Architecture
Nodes in the ad hoc routing zone broadcast RouteRequest packets in order to find a path to the destination.
Every intermediate node that receives the packet forwards it further until the packet reaches the destination.
When the destination node receives the packet, it responds by sending back a RouteReply packet.
In Meghadoot, the routing overhead is reduced whenever INs are present.
Whenever a GN receives a RouteRequest packet, instead of flooding, it forwards the packet to the IN.

## Slide 8: The Meghadoot Architecture
If the destination node lies in its control zone, the IN returns the path information to the GN using a RouteReply packet.
The GN receives the RouteReply packet and forwards to the original sender node.
Using the IBAR protocol, the IN maintains the approximate topology of the nodes within its zone.
When a path break is detected by the sender node, it sends a new RouteRequest packet to the IN for reconfiguring the broken path.
If an intermediate node detects a path break, it sends a RouteError packet to the IN, upon reception of which the IN obtains a new path and informs the sender.

## Slide 9: The 802.11phone
The end user equipment in Meghadoot is an IEEE 802.11 enabled device, either a laptop computer with an 802.11 adapter, or a small handheld device with an 802.11 interface.
Meghadoot is aimed at deployment in rural areas, where other communication infrastructure is not available, using an 802.11phone (an inexpensive handheld device with an 802.11b card).
The actual usage of Meghadoot not only aims at voice communication, but also aids the rural community to utilize other applications, such as data gathering, accounting, limited data processing, and for using local language-based applications.

## Slide 10: The 802.11phone
The software architecture of 802.11phone used in the Meghadoot system.

## Slide 11: The 802.11phone
Therefore, Meghadoot utilized the Picopeta Simputer (Version 3) as one of the devices for implementation of the 802.11phone.
Above figure shows the software components used in the 802.11phone, implemented with Meghadoot.
For voice communication, a Linux-based voice-over IP (VoIP) protocol stack that works with TCP/IP is used.

## Slide 12: The 802.11phone
Meghadoot aims at providing community networking for voice or data over multi-hop wireless networks, with or without the use of infrastructure nodes.
Meghadoot envisions the usage of a simple bicycle dynamo for powering the 802.11phone.